INTERNATIONAL ORGANISATION FOR STANDARDISATION

ORGANISATION INTERNATIONALE DE NORMALISATION

ISO/IEC JTC1/SC29/WG11

CODING OF MOVING PICTURES AND ASSOCIATED AUDIO

ISO/IEC JTC1/SC29/WG11 N0702rev

Incorporating N702 Delta of 24 March

25 March 1994

Video

INFORMATION TECHNOLOGY -

GENERIC CODING OF MOVING PICTURES AND ASSOCIATED AUDIO

Recommendation H.262

ISO/IEC 13818-2

Draft International Standard

Draft of:	10:18 Friday 25 March 1994

CONTENTS

CONTENTS	i

Foreword	iii

I	Introduction	iv

I.1	Purpose	iv

I.2	Application	iv

I.3	Profiles and levels	iv

I.4	The scalable and the non-scalable syntax	v

1	Scope	1

2	Normative references	1

3	Definitions	3

4	Abbreviations and symbols	9

4.1	Arithmetic operators	9

4.2	Logical operators	9

4.3	Relational operators	9

4.4	Bitwise operators	10

4.5	Assignment	10

4.6	Mnemonics	10

4.7	Constants	10

5	Conventions	11

5.1	Method of describing bitstream syntax	11

5.2	Definition of functions	12

5.3	Reserved, forbidden and marker_bit	12

5.4	Arithmetic precision	12

6	Video bitstream syntax and semantics	13

6.1	Structure of coded video data	13

6.2	Video bitstream syntax	25

6.3	Video bitstream semantics	39

7	The video decoding process	63

7.1	Higher syntactic structures	63

7.2	Variable length decoding	64

7.3	Inverse scan	67

7.4	Inverse quantisation	68

7.5	Inverse DCT	73

7.6	Motion compensation	73

7.7	Spatial scalability	90

7.8	SNR scalability	103

7.9	Temporal scalability	109

7.10	Data partitioning	113

7.11	Hybrid scalability	115

7.12	Output of the decoding process	116

8	Profiles and levels	119

8.1	ISO/IEC 11172-2 compatibility	120

8.2	Relationship between defined profiles	120

8.3	Relationship between defined levels	122

8.4	Scalable layers	123

8.4.1	Permissible layer combinations	124

8.5	Parameter values for defined profiles, levels and layers	126

Annex A  Discrete cosine transform	131

Annex B  Variable length code tables	132

B.1	Macroblock addressing	132

B.2	Macroblock type	133

B.3	Macroblock pattern	138

B.4	Motion vectors	139

B.5	DCT coefficients	140

Annex C  Video buffering verifier	149

Annex D  Features supported by the algorithm	154

D.1	Overview	154

D.2	Video Formats	154

D.3	Picture Quality	155

D.4	Data Rate Control	155

D.5	Low Delay Mode	156

D.6	Random Access/Channel Hopping	156

D.7	Scalability	156

D.8	Compatibility	164

D.9	Differences bewteen this specification and ISO/IECÊ11172-2	164

D.10	Complexity	167

D.11	Editing Encoded Bitstreams	167

D.12	Trick modes	167

D.13	Error Resilience	169

Annex E  Profile and level restrictions	178

E.1	Syntax element restrictions in profiles	178

E.2	Permissible layer combinations  (see 8.4.1)	189

Annex F  Patent statements	192

Annex G  Bibliography	194

Foreword

The ITU-T (the ITU Telecommunication Standardisation Sector) is a permanent organ of the International Telecommunications Union (ITU). The ITU-T is responsible for studying technical, operating and tariff questions and issuing Recommendations on them with a view to developing telecommunication standards on a world-wide basis.

The World Telecommunication Standardisation Conference, which meets every four years, establishes the program of work arising from the review of existing questions and new questions among other things. The approval of new or revised Recommendations by members of the ITU-T is covered by the procedure laid down in the ITU-T Resolution No. 1 (Helsinki 1993).  The proposal for Recommendation is accepted if 70% or more of the replies from members indicate approval.

ISO (the International Organisation for Standardisation) and IEC (the International Electrotechnical Commission) form the specialised system for world-wide standardisation.  National Bodies that are members of ISO and IEC participate in the development of International Standards through technical committees established by the respective organisation to deal with particular fields of technical activity.  ISO and IEC technical committees collaborate in fields of mutual interest.  Other international organisations, governmental and non-governmental, in liaison with ISO and IEC, also take part in the work.

In the field of information technology, ISO and IEC have established a joint technical committee, ISO/IEC JTC1.  Draft International Standards adopted by the joint technical committee are circulated to national bodies for voting.  Publication as an International Standard requires approval by at least 75% of the national bodies casting a vote.

This specification is a committee draft that is being submitted for approval to the ITU-T, ISO-IEC/JTC1 SC29. It was prepared jointly by SC29/WG11, also known as MPEG (Moving Pictures Expert Group), and the Experts Group for ATM Video Coding in the ITU-T SG15. MPEG was formed in 1988 to establish standards for coding of moving pictures and associated audio for various applications such as digital storage media, distribution and communication.  The Experts Group for ATM Video Coding was formed in 1990 to develop video coding standard(s) appropriate for B-ISDN using ATM transport.

In this specification Annex A, Annex B and Annex C contain normative requirements and are an integral part of this specification. Annex D, Annex E, Annex F and Annex G are informative and contain no normative requirements.

ISO/IEC

This International Standard is published in four Parts.

13818-1 systems Ñ	specifies the system coding of the specification. It defines a multiplexed structure for combining audio and video data and means of representing the timing information needed to replay synchronised sequences in real-time.

13818-2 video Ñ	specifies the coded representation of video data and the decoding process required to reconstruct pictures.

13818-3 audio Ñ	specifies the coded representation of audio data.

13818-4 conformanceÑ	specifies the procedures for determining the characteristics of coded bitstreams and for testing compliance with the requirements stated in 13818-1, 13818-2 and 13818-3.

I	Introduction

I.1	Purpose

This Part of this specification was developed in response to the growing need for a generic coding method of moving pictures and of associated sound for various applications such as digital storage media, television broadcasting and communication. The use of this specification means that motion video can be manipulated as a form of computer data and can be stored on various storage media, transmitted and received over existing and future networks and distributed on existing and future broadcasting channels.

I.2	Application

The applications of this specification cover, but are not limited to, such areas as listed below:

BSS	Broadcasting Satellite Service (to the home)

CATV	Cable TV Distribution on optical networks, copper, etc.

CDAD	Cable Digital Audio Distribution

DAB	Digital Audio Broadcasting (terrestrial and satellite broadcasting)

DTTB	Digital Terrestrial Television Broadcast

EC	Electronic Cinema

ENG	Electronic News Gathering (including SNG, Satellite News Gathering)

FSS	Fixed Satellite Service (e.g. to head ends)

HTT	Home Television Theatre

IPC	Interpersonal Communications (videoconferencing, videophone, etc.)

ISM	Interactive Storage Media (optical disks, etc.)

MMM	Multimedia Mailing

NCA	News and Current Affairs

NDB	Networked Database Services (via ATM, etc.)

RVS	Remote Video Surveillance

SSM	Serial Storage Media (digital VTR, etc.)

I.3	Profiles and levels

This specification is intended to be generic in the sense that it serves a wide range of applications, bitrates, resolutions, qualities and services.  Applications should cover, among other things, digital storage media, television broadcasting and communications.  In the course of creating this specification, various requirements from typical applications have been considered, necessary algorithmic elements have been developed, and they have been integrated into a single syntax.  Hence this specification will facilitate the bitstream interchange among different applications.

Considering the practicality of implementing the full syntax of this specification, however, a limited number of subsets of the syntax are also stipulated by means of "profile" and "level".  These and other related terms are formally defined in clauseÊ 3 of this specification.

A ÒprofileÓ is a defined subset of the entire bitstream syntax that is defined by this specification.  Within the bounds imposed by the syntax of a given profile it is still possible to require a very large variation in the performance of encoders and decoders depending upon the values taken by parameters in the bitstream.  For instance it is possible to specify frame sizes as large as (approximately) 214 samples wide by 214 lines high.  It is currently neither practical nor economic to implement a decoder capable of dealing with all possible frame sizes.

In order to deal with this problem ÒlevelsÓ are defined within each profile.  A level is a defined set of constraints imposed on parameters in the bitstream.  These constraints may be simple limits on numbers.  Alternatively they may take the form of constraints on arithmetic combinations of the parameters (e.g. frame width multiplied by frame height multiplied by frame rate).

Bitstreams complying with this specification use a common syntax.  In order to achieve a subset of the complete syntax flags and parameters are included in the bitstream that signal the presence or otherwise of syntactic elements that occur later in the bitstream.  In order to specify constraints on the syntax (and hence define a profile) it is thus only necessary to constrain the values of these flags and parameters that specify the presence of later syntactic elements.

I.4	The scalable and the non-scalable syntax

The full syntax can be divided into two major categories: One is the non-scalable syntax, which is structured as a super set of the syntax defined in ISO/IECÊ11172-2.  The main feature of the non-scalable syntax is the extra compression tools for interlaced video signals.  The second is the scalable syntax, the key property of which is to enable the reconstruction of useful video from pieces of a total bitstream.  This is achieved by structuring the total bitstream in two or more layers, starting from a standalone base layer and adding a number of enhancement layers.  The base layer can use the non-scalable syntax, or in some situations conform to the ISO/IEC 11172-2 syntax.

I.4.1	Overview of the non-scalable syntax

The coded representation defined in the non-scalable syntax achieves a high compression ratio while preserving good image quality. The algorithm is not lossless as the exact sample values are not preserved during coding. Obtaining good image quality at the bitrates of interest demands very high compression, which is not achievable with intra picture coding alone. The need for random access, however, is best satisfied with pure intra picture coding. The choice of the techniques is based on the need to balance a high image quality and compression ratio with the requirement to make random access to the coded bitstream.

A number of techniques are used to achieve high compression. The algorithm first uses block-based motion compensation to reduce the temporal redundancy. Motion compensation is used both for causal prediction of the current picture from a previous picture, and for non-causal, interpolative prediction from past and future pictures. Motion vectors are defined for each 16-sample by 16-line region of the picture. The difference signal, i.e., the prediction error, is further compressed using the discrete cosine transform (DCT) to remove spatial correlation before it is quantised in an irreversible process that discards the less important information. Finally, the motion vectors are combined with the residual DCT information, and encoded using variable length codes.

I.4.1.1	Temporal processing

Because of the conflicting requirements of random access and highly efficient compression, three main picture types are defined. Intra coded pictures (I-Pictures) are coded without reference to other pictures. They provide access points to the coded sequence where decoding can begin, but are coded with only moderate compression. Predictive coded pictures (P-Pictures) are coded more efficiently using motion compensated prediction from a past intra or predictive coded picture and are generally used as a reference for further prediction. Bidirectionally-predictive coded pictures (B-Pictures) provide the highest degree of compression but require both past and future reference pictures for motion compensation. Bidirectionally-predictive coded pictures are never used as references for prediction (except in the case that the resulting picture is used as a reference in a spatially scalable enhancement layer). The organisation of the three picture types in a sequence is very flexible. The choice is left to the encoder and will depend on the requirements of the application. Figure I-1 illustrates the relationship among the three different picture types.

Figure I-1 Example of temporal picture structure

I.4.1.2	Coding interlaced video

Each frame of interlaced video consists of two fields which are separated by one field-period. The specification allows either the frame to be encoded as picture or the two fields to be encoded as two pictures.  Frame encoding or field encoding can be adaptively selected on a frame-by-frame basis.  Frame encoding is typically preferred when the video scene contains significant detail with limited motion.  Field encoding, in which the second field can be predicted from the first, works better when there is fast movement.

I.4.1.3	Motion representation - macroblocks

As in ISO/IEC 11172-2, the choice of 16 by 16 macroblocks for the motion-compensation unit is a result of the trade-off between the coding gain provided by using motion information and the overhead needed to represent it. Each macroblock can be temporally predicted in one of a number of different ways.  For example, in frame encoding, the prediction from the previous reference frame can itself be either frame-based or field-based. Depending on the type of the macroblock, motion vector information and other side information is encoded with the compressed prediction error signal in each macroblock. The motion vectors are encoded differentially with respect to the last encoded motion vectors using variable length codes. The maximum length of the motion vectors that may be represented can be programmed, on a picture-by-picture basis, so that the most demanding applications can be met without compromising the performance of the system in more normal situations.

It is the responsibility of the encoder to calculate appropriate motion vectors. The specification does not specify how this should be done.

I.4.1.4	Spatial redundancy reduction

Both original pictures and prediction error signals have high spatial redundancy. This specification uses a block-based DCT method with visually weighted quantisation and run-length coding. After motion compensated prediction or interpolation, the residual picture is split into 8 by 8 blocks. These are transformed into the DCT domain where they are weighted before being quantised. After quantisation many of the coefficients are zero in value and so two-dimensional run-length and variable length coding is used to encode the remaining coefficients efficiently.

I.4.1.5	Chrominance formats

In addition to the 4:2:0 format supported in ISO/IECÊ11172-2 this specification supports 4:2:2 and 4:4:4 chrominance formats.

I.4.2	Scalable extensions

The scalability tools in this specification are designed to support applications beyond that supported by single layer video. Among the noteworthy applications areas addressed are video telecommunications, video on asynchronous transfer mode networks (ATM), interworking of video standards,  video service hierarchies with multiple spatial, temporal and quality resolutions, HDTV with embedded TV, systems allowing migration to higher temporal resolution HDTV etc. Although a simple solution to scalable video is the simulcast technique which is based on transmission/storage of multiple independently coded reproductions of video, a more efficient alternative is scalable video coding, in which the bandwidth allocated to a given reproduction of video can be partially reutilised in coding of the next reproduction of video.  In scalable video coding, it is assumed that given an encoded bitstream, decoders of various complexities can decode and display appropriate reproductions of coded video.  A scalable video encoder is likely to have increased complexity when compared to a single layer encoder. However, this standard provides several different forms of scalabilities that address nonoverlapping applications with corresponding complexities. The basic scalability tools offered are: data partitioning, SNR scalability, spatial scalability and  temporal scalability. Moreover, combinations of these basic scalability tools are also supported and are referred to as hybrid scalability. In the case of basic scalability, two layers of video referred to as the lower layer  and the enhancement layer  are allowed, whereas in hybrid scalability up to three layers are supported. The following Tables provide a few example applications of various scalabilities.

TableÊI-1 Applications of SNR scalability

| Lower layer | Enhancement layer | Application |  | ITU-R-601 | Same resolution and format as lower layer | Two quality service for Standard TV |  | High Definition | Same resolution and format as lower layer | Two quality service for HDTV |  | 4:2:0 High Definition | 4:2:2 chroma simulcast | Video production / distribution |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

TableÊI-2 Applications of spatial scalability

| Base | Enhancement | Application |  | progressive(30Hz) | progressive(30Hz) | CIF/SCIF compatibility or scalability |  | interlace(30Hz) | interlace(30Hz) | HDTV/SDTV scalability |  | progressive(30Hz) | interlace(30Hz) | ISO/IECÊ11172-2/compatibility with this specification |  | interlace(30Hz) | progressive(60Hz) | Migration to HR progressive HDTV |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

TableÊI-3. Applications of temporal scalability

| Base | Enhancement | Higher | Application |  | progressive(30Hz) | progressive(30Hz) | progressive (60Hz) | Migration to HR progressive HDTV |  | interlace(30Hz) | interlace(30Hz) | progressive (60Hz) | Migration to HR progressive HDTV |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

I.4.2.1	Spatial scalable extension

Spatial scalability is a tool intended for use in video applications involving telecommunications, interworking of video standards, video database browsing, interworking of HDTV and TV etc., i.e., video systems with the primary common feature that a minimum of two layers of spatial resolution are necessary. Spatial scalability involves generating two spatial resolution video layers from a single video source such that the lower layer is coded by itself to provide the basic spatial resolution and the enhancement layer employs the spatially interpolated lower layer and carries the full spatial resolution of the input video source. The lower and the enhancement layers may either both use the coding tools in this specification, or the ISO/IECÊ11172-2 standard for the lower layer and this specification for the enhancement layer. The latter case achieves a further advantage by facilitating interworking between video coding standards. Moreover, spatial scalability offers flexibility in choice of video formats to be employed in each layer. An additional advantage of spatial scalability is its ability to provide resilience to transmission errors as the more important data of the lower layer can be sent over channel with better error performance, while the less critical enhancement layer data can be sent over a channel with poor error performance.

I.4.2.2	SNR scalable extension

SNR scalability is a tool intended for use in video applications involving telecommunications, video services with multiple qualities,  standard TV and HDTV, i.e., video systems with the primary common feature that a minimum of two layers of video quality are necessary. SNR scalability involves generating two video layers of same spatial resolution but different video qualities from a single video source such that the lower layer is coded by itself to provide the basic video quality and the enhancement layer is coded to enhance the lower layer.  The enhancement layer when added back to the lower layer regenerates a higher quality reproduction of the input video. The lower and the enhancement layers may either use this specification or ISO/IECÊ11172-2 standard for the lower layer and this specification for the enhancement layer. An additional advantage of SNR scalability is its ability to provide high degree of resilience to transmission errors as the more important data of the lower layer can be sent over channel with better error performance, while the less critical enhancement layer data can be sent over a channel with poor error performance.

I.4.2.3	Temporal scalable extension

Temporal scalability is a tool intended for use in a range of diverse video applications from telecommunications to HDTV for which migration to higher temporal resolution systems from that of  lower temporal resolution systems may be necessary. In many cases, the lower temporal resolution video systems may be either the existing systems or the less expensive early generation systems, with the motivation of introducing  more sophisticated systems gradually. Temporal scalability involves partitioning of video frames into layers, whereas the lower layer is coded by itself to provide the basic temporal rate and the enhancement layer is coded with temporal prediction with respect to the lower layer, these layers when decoded and temporal multiplexed to yield full temporal resolution of the video source.  The lower temporal resolution systems may only decode the lower layer to provide basic temporal resolution, whereas more sophisticated systems of the future may decode both layers and provide high temporal resolution video while maintaining interworking with earlier generation systems. An additional advantage of temporal scalability is its ability to provide  resilience to transmission errors as the more important data of the lower layer can be sent over channel with better error performance, while the less critical enhancement layer can be sent over a channel with poor error performance.

I.4.2.4	Data partitioning extension

Data partitioning  is a tool intended for use when two channels are available for transmission and/or storage of a video bitstream, as may be the case in ATM networks, terrestrial broadcast, magnetic media, etc.  The bitstream is partitioned between these channels such that more critical parts of the bitstream (such as headers, motion vectors, DC coefficients) are transmitted in the channel with the better error performance, and less critical data (such as higher DCT coefficients) is transmitted in the channel with poor error performance. Thus, degradation to channel errors are minimised since the critical parts of a bitstream are better protected.  Data from neither channel may be decoded on a decoder that is not intended for decoding data partitioned bitstreams.

INTERNATIONAL STANDARD 13818-2

ITU-T RECOMMENDATION H.262

INFORMATION TECHNOLOGY -

GENERIC CODING OF MOVING PICTURES AND ASSOCIATED AUDIO

1	Scope

This Recommendation | International Standard specifies the coded representation of picture information for digital storage media and digital video communication and specifies the decoding process. The representation supports constant bitrate transmission, variable bitrate transmission, random access, channel hopping, scalable decoding, bitstream editing, as well as special functions such as fast forward playback, fast reverse playback, slow motion, pause and still pictures. This Recommendation | International Standard is forward compatible with ISO/IECÊ11172-2 and upward or downward compatible with EDTV, HDTV, SDTV formats.

This Recommendation | International Standard is primarily applicable to digital storage media, video broadcast and communication. The storage media may be directly connected to the decoder, or via communications means such as busses, LANs, or telecommunications links.

2	Normative references

The following ITU-T Recommendations and International Standards contain provisions which through reference in this text, constitute provisions of this Recommendation | International Standard. At the time of publication, the editions indicated were valid. All Recommendations and Standards are subject to revision, and parties to agreements based on this Recommendation | International Standard are encouraged to investigate the possibility of applying the most recent editions of the standards indicated below. Members of IEC and ISO maintain registers of currently valid International Standards. The TSB (Telecommunication Standardisation Bureau) maintains a list of currently valid ITU-T Recommendations.

¥	Recommendations and reports of the CCIR, 1990

XVIIth Plenary Assembly, Dusseldorf, 1990	Volume XI - Part 1

Broadcasting Service (Television)	Rec. 601-2 "Encoding parameters of digital television for studios"

¥	CCIR Volume X and XI Part 3	Recommendation 648: Recording of audio signals.

¥	CCIR Volume X and XI Part 3	Report 955-2: Sound broadcasting by satellite for portable and mobile receivers, including Annex IV Summary description of advanced digital system II.

¥	ISO/IEC 11172 (1993)	"Information technology Ñ Coding of moving picture and associated audio for digital storage media at up to about 1,5 Mbit/s"

¥	IEEE Standard Specifications for the Implementations of 8 by 8 Inverse Discrete Cosine Transform, IEEE Std 1180-1990, December 6, 1990.

¥	IEC Publication 908:198, "CD Digital Audio System"

¥	IEC Standard Publication 461 Second edition, 1986	"Time and control code for video tape recorders"

¥	ITU-T Recommendation H.261 (Formerly CCITT Recommendation H.261) ÒCodec for audiovisual services at px64 kbit/s" Geneva, 1990

¥	ISO/IEC 10918-1 | ITU-T Rec. T.81 (JPEG) "Digital compression and coding of continuous-tone still images"

3	Definitions

For the purposes of this Recommendation | International Standard, the following definitions apply.

3.1	AC coefficient: Any DCT coefficient for which the frequency in one or both dimensions is non-zero.

3.2	B-field picture: A field structure B-Picture.

3.3	B-frame picture: A frame structure B-Picture.

3.4	B-picture; bidirectionally predictive-coded picture:  A picture that is coded using motion compensated prediction from past and/or future reference fields or frames.

3.5	backward compatibility: A newer coding standard is  backward compatible with an older coding standard if decoders designed to operate with the older coding standard are able to continue to operate by decoding all or part of a bitstream produced according to the newer coding standard.

3.6	backward motion vector: A motion vector that is used for motion compensation from a reference frame or reference field at a later time in display order.

3.7	bidirectionally predictive-coded picture; B-picture: A picture that is coded using motion compensated prediction from past and/or future reference frames or reference fields.

3.8	bitrate:  The rate at which the coded bitstream is delivered from the storage medium to the input of a decoder.

3.9	block: An 8-row by 8-column matrix of samples, or 64  DCT coefficients (source, quantised or dequantised).

3.10	bottom field: One of two fields that comprise a frame. Each line of a bottom field is spatially located immediately below the corresponding line of the top field.

3.11	byte aligned: A bit in a coded bitstream is byte-aligned if its position is a multiple of 8-bits from the first bit in the stream.

3.12	byte: Sequence of 8-bits.

3.13	channel: A digital medium that stores or transports a bitstream constructed according to this specification.

3.14	chrominance  format:  Defines  the number of chrominance blocks in a macroblock.

3.15	chroma simulcast: A type of scalability  (which is a subset of SNR scalability) where  the enhancement layer (s) contain only coded refinement  data  for the  DC coefficients, and all the data for the AC coefficients, of the chrominance components.

3.16	chrominance (component): A matrix, block or single sample representing one of the two colour difference signals related to the primary colours in the manner defined in the bitstream. The symbols used for the chrominance signals are Cr and Cb.

3.17	coded B-frame: A B-frame picture or a pair of B-field pictures.

3.18	coded frame: A coded frame is a coded I-frame, a coded P-frame or a coded B-frame.

3.19	coded I-frame: An I-frame picture or a pair of field pictures, where the first one is an I-picture and the second one is an I-picture or a P-picture.

3.20	coded P-frame: A P-frame picture or a pair of P-field pictures.

3.21	coded picture: A coded picture is made of a picture header, the optionnal extensions immediately following it, and the following picture data.  A coded picture may be a frame picture or a field picture.

3.22	coded video bitstream: A coded representation of a series of one or more pictures as defined in this specification.

3.23	coded order: The order in which the pictures are transmitted and decoded.  This order is not necessarily the same as the display order.

3.24	coded representation: A data element as represented in its encoded form.

3.25	coding parameters: The set of user-definable parameters that characterise a coded video bitstream.  Bitstreams are characterised by coding parameters.  Decoders are characterised by the bitstreams that they are capable of decoding.

3.26	component: A matrix, block or single sample from one of the three matrices (luminance and two chrominance) that make up a picture.

3.27	compression: Reduction in the number of bits used to represent an item of data.

3.28	constant bitrate coded video:  A compressed video bitstream with a constant average bitrate.

3.29	constant bitrate:  Operation where the bitrate is constant from start to finish of the coded bitstream.

3.30	data element: An item of data as represented before encoding and after decoding.

3.31	data partitioning:  A method for dividing a bitstream into two separate bitstreams  for  error resilience purposes.  the two bitstreams have to be recombined before decoding.

3.32	D-Picture: A type of picture that shall not be used except in ISO/IECÊ11172-2.

3.33	DC coefficient: The DCT coefficient for which the frequency is zero in both dimensions.

3.34	DCT coefficient: The amplitude of a specific cosine basis function.

3.35	decoder input buffer: The first-in first-out  (FIFO) buffer specified in the video buffering verifier.

3.36	decoder: An embodiment of a decoding process.

3.37	decoding (process): The process defined in this specification that reads an input coded bitstream and produces decoded pictures or audio samples.

3.38	dequantisation: The process of rescaling the quantised DCT coefficients after their representation in the bitstream has been decoded and before they are presented to the inverse DCT.

3.39	digital storage media; DSM: A digital storage or transmission device or system.

3.40	discrete cosine transform; DCT: Either the forward discrete cosine transform or the inverse discrete cosine transform.  The DCT is an invertible, discrete orthogonal transformation.  The inverse DCT is defined in Annex A of this specification.

3.41	display order: The order in which the decoded pictures are displayed.  Normally this is the same order in which they were presented at the input of the encoder.

3.42	editing: The process by which one or more coded bitstreams are manipulated to produce a new coded bitstream.  Conforming edited bitstreams must meet the requirements defined in this specification.

3.43	encoder: An embodiment of an encoding process.

3.44	encoding (process): A process, not specified in this specification, that reads a stream of input pictures or audio samples and produces a valid coded bitstream as defined in this specification.

3.45	fast forward playback: The process of displaying a sequence, or parts of a sequence, of pictures in display-order faster than real-time.

3.46	fast  reverse playback: The process of displaying the picture sequence in the reverse of display order faster than real-time.

3.47	field: For an interlaced  video signal, a ÒfieldÓ is the assembly of alternate lines of a frame. Therefore an interlaced frame is composed of two fields, a top field and a bottom field.

3.48	field period:  The reciprocal of twice the frame rate.

3.49	field picture; field structure picture : A field structure picture is a coded picture with picture_structure is equal to "Top field" or "Bottom field".

3.50	flag: A variable which can take one of only the two values defined in this specification.

3.51	forbidden: The term "forbidden" when used in the clauses defining the coded bitstream indicates that the value shall never be used.  This is usually to avoid emulation of start codes.

3.52	forced updating: The process by which macroblocks are intra-coded from time-to-time to ensure that mismatch errors between the inverse DCT processes in encoders and decoders cannot build up excessively.

3.53	forward compatibility: A newer coding standard is forward compatible with an older coding standard if decoders designed to operate with the newer coding standard are able to decode bitstreams of the older coding standard.

3.54	forward motion vector: A motion vector that is used for motion compensation from a reference frame or reference field at an earlier time in display order.

3.55	frame: A frame contains lines of spatial information of a video signal. For progressive video, these lines contain samples starting from one time instant and continuing through successive lines to the bottom of the frame.  For interlaced video a frame consists of two fields, a top field and a bottom field.  One of these fields will commence one field period later than the other.

3.56	frame period:  The reciprocal of the  frame rate.

3.57	frame picture; frame structure picture : A frame structure picture is a coded picture with picture_structure is equal to "Frame".

3.58	frame rate: The rate at which frames are be output from the decoding process.

3.59	future reference frame (field):  A future reference frame(field) is a reference frame(field) that occurs at a later time than the current picture in display order.

3.60	header: A block of data in the coded bitstream containing the coded representation of a number of data elements pertaining to the coded data that follow the header in the bitstream.

3.61	hybrid scalability:  Hybrid scalability is the combination  of two (or more) types of scalability.

3.62	interlace: The property of conventional television frames where alternating lines of the frame represent different instances in time.  In an interlaced frame, one of the field is meant to be displayed first. This field is called the first field.  The first field can be the top field or the bottom field of the frame.

3.63	I-field picture: A field structure I-Picture.

3.64	I-frame picture: A frame structure I-Picture.

3.65	I-picture; intra-coded picture: A picture coded using information only from itself.

3.66	intra coding: Coding of a macroblock or picture that uses information only from that macroblock or picture.

3.67	intra-coded picture; I-picture: A picture coded using information only from itself.

3.68	level : A defined set of constraints on the values which may be taken by the parameters of this specification within a particular profile.  A profile may contain one or more levels.

3.69	luminance (component): A matrix, block or single sample representing a monochrome representation of the signal and related to the primary colours in the manner defined in  the bitstream. The symbol used for luminance is Y.

3.70	macroblock: The four 8 by 8 blocks of luminance data and the two (for  4:2:0 chrominance format), four (for  4:2:2 chrominance format) or eight (for  4:4:4  chrominance format) corresponding 8 by 8 blocks of chrominance data coming from a 16 by 16 section of the luminance component of the picture.  Macroblock is sometimes used to refer to the sample data and sometimes to the coded representation of the sample values and other data elements defined in the macroblock header of the syntax defined in this part of this specification.  The usage is clear from the context.

3.71	motion compensation: The use of motion vectors to improve the efficiency of the prediction of sample values.  The prediction uses motion vectors to provide offsets into the past and/or future reference frames or reference fields containing previously decoded sample values that are used to form the prediction error signal.

3.72	motion estimation: The process of estimating motion vectors during the encoding process.

3.73	motion vector: A two-dimensional vector used for motion compensation that provides an offset from the coordinate position in the current picture or field to the coordinates in a reference frame or reference field.

3.74	non-intra coding: Coding of a macroblock or picture that uses information both from itself and from macroblocks and pictures occurring at other times.

3.75	P-field picture: A field structure P-Picture.

3.76	P-frame picture: A frame structure P-Picture.

3.77	P-picture; predictive-coded picture : A picture that is coded using motion compensated prediction from past reference fields or frame.

3.78	parameter: A variable within the syntax of this specification which may take one of a large range of values.  A variable which can take one of only two values is a flag and not a parameter.

3.79	past reference frame (field):  A past reference frame(field) is a reference frame(field) that occurs at an earlier time than the current picture in display order.

3.80	picture: Source, coded or reconstructed image data. A source or reconstructed picture consists of three rectangular matrices of 8-bit numbers representing the luminance and two chrominance signals. For progressive video, a picture is identical to a frame, while for interlaced video, a picture can refer to a frame, or the top field or the bottom field of the frame depending on the context.

3.81	prediction: The use of a predictor to provide an estimate of the sample value or data element currently being decoded.

3.82	predictive-coded picture; P-picture: A picture that is coded using motion compensated prediction from past reference frames or reference fields.

3.83	prediction error: The difference between the actual value of a sample or data element and its predictor.

3.84	predictor: A linear combination of previously decoded sample values or data elements.

3.85	profile: A defined subset of the syntax of this specification.

Note	In this specification the word ÒprofileÓ is used as defined above.  It should not be confused with other definitions of ÒprofileÓ and in particular it does not have the meaning that is defined by JTC1/SGFS.

3.86	progressive: The property of film frames where all the samples of the frame represent the same instances in time.

3.87	quantisation matrix: A set of sixty-four 8-bit values used by the dequantiser.

3.88	quantised DCT coefficients: DCT coefficients before dequantisation.  A variable length coded representation of quantised DCT coefficients is transmitted as part of the compressed video bitstream.

3.89	quantiser scale: A scale factor coded in the bitstream and used by the decoding process to scale the dequantisation.

3.90	random access: The process of beginning to read and decode the coded bitstream at an arbitrary point.

3.91	reconstructed frame: A reconstructed frame consists of three rectangular matrices of 8-bit numbers representing the luminance and two chrominance signals. A reconstructed frame is obtained by decoding a coded frame.

3.92	reconstructed picture: A reconstructed picture is obtained by decoding a coded picture. A reconstructed picture is either a reconstructed frame (when decoding a frame picture), or one field of a reconstructed frame (when decoding a field picture). If the coded picture is a field picture, then the reconstructed picture is the top field or the bottom field of the reconstructed frame.

3.93	reference  field: A reference field is one field of a reconstructed frame. Reference fields are used for forward and backward prediction when P-pictures and B-pictures are decoded. Note that when field P-pictures are decoded, prediction of the second field P-picture of a coded frame uses the first reconstructed field of the same coded frame as a reference field.

3.94	reference  frame: A reference frame is a reconstructed frame that was coded in the form of a coded I-frame or a coded P-frame.  Reference frames are used for forward and backward prediction when P-pictures and B-pictures are decoded.

3.95	reserved: The term "reserved" when used in the clauses defining the coded bitstream indicates that the value may be used in the future for ISO/IEC defined extensions.

3.96	sample aspect ratio: (abbreviated to SAR). This specifies the distance between samples. It is defined (for the purposes of this specification) as the vertical displacement of the lines of luminance samples in a frame divided by the horizontal displacement of the luminance samples. Thus its units are (metres per line) Ö (metres per sample)

3.97	scalability: Scalability  is the ability of  a decoder to decode an ordered set of bitstreams to produce a reconstructed sequence. Moreover, useful video is output when subsets are decoded.  The minimum subset  that can thus be decoded is the first bitstream in the set which is called the base layer.  Each of the other bitstreams in the set is called an enhancement layer.  When addressing a specific enhancement layer,  "lower layer" refer to the bitstream which precedes the enhancement layer.

3.98	side information: Information in the bitstream necessary for controlling the decoder.

3.99	skipped macroblock: A macroblock for which no data  is encoded.

3.100	slice: A series of macroblocks.

3.101	SNR scalability:  A type of scalability where  the enhancement layer (s) contain only coded refinement  data  for the  DCT coefficients of the lower layer.

3.102	spatial scalability: A type of scalability where an enhancement layer  also uses predictions from sample data derived from a lower layer without using motion vectors.  The layers can have different frame sizes, frame rates or chrominance formats

3.103	start codes [system and video]: 32-bit codes embedded in that coded bitstream that are unique.  They are used for several purposes including identifying some of the structures in the coding syntax.

3.104	stuffing (bits); stuffing (bytes) : Code-words that may be inserted into the coded bitstream that are discarded in the decoding process.  Their purpose is to increase the bitrate of the stream.

3.105	temporal scalability:  A type of scalability where an enhancement layer  also uses predictions from sample data derived from a lower layer  using motion vectors.  The layers  have identical frame size, and  chrominance formats, but can  have different frame rates.

3.106	top field: One of two fields that comprise a frame. Each line of a top field is spatially located immediately above the corresponding line of the bottom field.

3.107	variable bitrate:  Operation where the bitrate varies with time during the decoding of a coded bitstream.

3.108	variable length coding; VLC:  A reversible procedure for coding that assigns shorter code-words to frequent events and longer code-words to less frequent events.

3.109	video buffering verifier; VBV: A hypothetical decoder that is conceptually connected to the output of the encoder.  Its purpose is to provide a constraint on the variability of the data rate that an encoder or editing process may produce.

3.110	video sequence: The highest syntactic structure of coded video bitstreams. It contains a series of one or more  coded frames.

3.111	zig-zag scanning order: A specific sequential ordering of the DCT coefficients from (approximately) the lowest spatial frequency to the highest.

4	Abbreviations and symbols

The mathematical operators used to describe this specification are similar to those used in the C programming language. However, integer divisions with truncation and rounding are specifically defined. Numbering and counting loops generally begin from zero.

4.1	Arithmetic operators

+	Addition.

-	Subtraction (as a binary operator) or negation (as a unary operator).

++	Increment.

- -	Decrement.

Multiplication.

^	Power.

/	Integer division with truncation of the result toward zero. For example, 7/4 and -7/-4 are truncated to 1 and -7/4 and 7/-4 are truncated to -1.

//	Integer division with rounding to the nearest integer. Half-integer values are rounded away from zero unless otherwise specified. For example 3//2 is rounded to 2, and -3//2 is rounded to -2.

DIV	Integer division with truncation of the result toward minus infinity. For example 3ÊDIVÊ2 is rounded to 1, and -3ÊDIVÊ2 is rounded to -2.

Ö	Used to denote division in mathematical equations where no truncation or rounding is intended.

%	Modulus operator. Defined only for positive numbers.

Sign(  )

Abs(  )

4.2	Logical operators

||	Logical OR.

&&	Logical AND.

!	Logical NOT.

4.3	Relational operators

>	Greater than.

>=	Greater than or equal to.

<	Less than.

<=	Less than or equal to.

==	Equal to.

!=	Not equal to.

max [,...,] 	the maximum value in the argument list.

min [,...,] 	the minimum value in the argument list.

4.4	Bitwise operators

&	AND

|	OR

>>	Shift right with sign extension.

<<	Shift left with zero fill.

4.5	Assignment

=	Assignment operator.

4.6	Mnemonics

The following mnemonics are defined to describe the different data types used in the coded bitstream.

bslbf	Bit string, left bit first, where "left" is the order in which bit strings are written in the specification. Bit strings are written as a string of 1s and 0s within  single quote marks, e.g. '1000 0001'. Blanks within a bit string are for ease of reading and have no significance.

uimsbf	Unsigned integer, most significant bit first.

simsbf	Signed integer, in twos complement format, most significant (sign) bit first.

vlclbf	Variable length code, left bit first, where "left" refers to the order in which the VLC codes are written. The byte order of multibyte words is most significant byte first.

4.7	Constants

¹	3,141Ê592Ê653Ê59...

e	2,718Ê281Ê828Ê45...

5	Conventions

5.1	Method of describing bitstream syntax

The bitstream retrieved by the decoder is described in 6.2. Each data item in the bitstream is in bold type. It is described by its name, its length in bits, and a mnemonic for its type and order of transmission.

The action caused by a decoded data element in a bitstream depends on the value of that data element and on data elements previously decoded. The decoding of the data elements and definition of the state variables used in their decoding are described in 6.3. The following constructs are used to express the conditions when data elements are present, and are in normal type:

| while ( condition ) { | If the condition is true, then the group of data elements |  | data_element | occurs next in the data stream. This repeats until the |  | . . . | condition is not true. |  | } |  |  |  |  |  | do { |  |  | data_element | The data element always occurs at least once. |  | . . . |  |  | } while ( condition ) | The data element is repeated until the condition is not true. |  |  |  |  | if ( condition) { | If the condition is true, then the first group of data |  | data_element | elements occurs next in the data stream. |  | . . . |  |  | } else { | If the condition is not true, then the second group of data |  | data_element | elements occurs next in the data stream. |  | . . . |  |  | } |  |  |  |  |  | for ( i = 0; i < n; i++) { | The group of data elements occurs n times. Conditional |  | data_element | constructs within the group of data elements may depend |  | . . . | on the value of the loop control variable i, which is set to |  | } | zero for the first occurrence, incremented to one for the second occurrence, and so forth. |  |  |  |  | /* comment ... */ | Explanatory comment that may be deleted entirely without |  |  | in any way altering the syntax. |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

This syntax uses the 'C-codeÕ convention that a variable or expression evaluating to a non-zero value is equivalent to a condition that is true.  In many cases a literal string is used in a condition.  For example;

if ( scalable_mode == Òspatial scalabilityÓ ) ...

In such cases the literal string is that used to describe the value of the bitstream element in 6.3.  In this example, we see that Òspatial scalabilityÓ is defined in TableÊ6-10 to be represented by the two bit binary number Ô01Õ.

As noted, the group of data elements may contain nested conditional constructs. For compactness, the {} are omitted when only one data element follows.

data_element [n] 	data_element [n] is the n+1th element of an array of data.

data_element [m][n]	data_element [m][n] is the m+1, n+1th element of a two-dimensional array of data.

While the syntax is expressed in procedural terms, it should not be assumed that 6.2 implements a satisfactory decoding procedure. In particular, it defines a correct and error-free input bitstream. Actual decoders must include means to look for start codes in order to begin decoding correctly, and to identify errors, erasures or insertions while decoding. The methods to identify these situations, and the actions to be taken, are not standardised.

5.2	Definition of functions

Several utility functions for picture coding algorithm are defined as follows:

5.2.1	Definition of bytealigned() function

The function bytealigned () returns 1 if the current position is on a byte boundary, that is the next bit in the bitstream is the first bit in a byte. Otherwise it returns 0.

5.2.2	Definition of nextbits() function

The function nextbits () permits comparison of a bit string with the next bits to be decoded in the bitstream.

5.2.3	Definition of next_start_code() function

The next_start_code() function removes any zero bit and zero byte stuffing and locates the next start code.

| next_start_code() { | No. of bits | Mnemonic |  | while ( !bytealigned() ) |  |  |  | zero_bit | 1 | "0" |  | while ( nextbits() != '0000 0000 0000 0000 0000 0001' ) |  |  |  | zero_byte | 8 | "0000 0000" |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

This function checks whether the current position is byte aligned. If it is not, zero stuffing bits are present. After that any number of zero bytes may be present before the start code. Therefore start codes are always byte aligned and may be preceded by any number of zero stuffing bits.

5.3	Reserved, forbidden and marker_bit

The terms "reserved" and "forbidden" are used in the description of some values of several fields in the coded bitstream.

The term "reserved" indicates that the value may be used in the future for ISO/IEC-defined extensions.

The term "forbidden" indicates a value that shall never be used (usually in order to avoid emulation of start codes).

The term "marker_bit" indicates a one bit field in which the value zero is forbidden.  These marker bits are introduced at several points in the syntax to avoid start code emulation.

5.4	Arithmetic precision

In order to reduce discrepancies between implementations of this specification, the following rules for arithmetic operations are specified.

(a)	Where arithmetic precision is not specified, such as in the calculation of the IDCT, the precision shall be sufficient so that significant errors do not occur in the final integer values

(b)	Where ranges of values are given by two dots, the end points are included if a bracket is present, and excluded if the 'less then' (<) and 'greater then' (>) characters are used. For example, [a .. b> means from a to b, including a but excluding b.

6	Video bitstream syntax and semantics

6.1	Structure of coded video data

Coded video data consists of an ordered set of video bitstreams, called layers.  If there is only one layer, the coded video data is called non-scalable video bitstream.  If there are two layers or more, the coded video data is called a scalable hierarchy.

The first layer (of the ordered set) is called base layer, and it can always be decoded independently.  See 7.1 to 7.6 of this specification for a description of the decoding process for the base layer, except in the case of Data partitionning, described in 7.10.

Other layers are called enhancement layers, and can only be decoded together with all the lower layers (previous layers in the ordered set), starting with the base layer. See 7.7 to 7.11 of this specification for a description of the decoding process for scalable hierarchy.

See ITU-TÊRec.ÊxxxÊ|ÊISO/IECÊ13818-1 for a description of the way layers may be multiplexed together.

The base layer of a scalable hierarchy may conform to this specification or to other standards such as ISO/IEC 11172-2.  See details in 7.7 to 7.11.  Enhancement layers shall conform to this specification.

In all cases apart from Data partitioning, the base layer does not contain a sequence_scalable_extension().  Enhancement layers always contain sequence_scalable_extension().

In general the video bitstream can be thought of as a syntactic hierarchy in which syntactic structures contain one or more subordinate structures.  For instance the structure Òpicture_data()Ó contains one or more of the syntactic structure Òslice()Ó which in turn contains one or more of the structure Òmacroblock()Ó.

This structure is very similar to that used in ISO/IEC 11172-2.

6.1.1	Video sequence

The highest syntactic structure of the coded video bitstream is the video sequence.

A video sequence commences with a sequence header which may optionally be followed by a group of pictures header and then by one or more coded frames.  The order of the coded frames in the coded bitstream is the order in which the decoder processes them, but not necessarily in the correct order for display.  The video sequence is terminated by a sequence_end_code.  At various points in the video sequence a particular coded frame may be preceded by either a repeat sequence header or a group of pictures header or both.  (In the case that both a repeat sequence header and a group of pictures header immediately precede a particular picture the group of pictures header shall follow the repeat sequence header.)

6.1.2.5	Progressive and interlaced sequences

This specification deals with coding of both progressive and interlaced sequences.

The output of the decoding process, for interlaced sequences, consists of a series of reconstructed fields that are separated in time by a field period.  The two fields of a frame may be coded separately (field-pictures).  Alternatively the two fields may be coded together as a frame (frame-pictures).  Both frame pictures and field pictures may be used in a single video sequence.

In progressive sequences each picture in the sequence shall be a frame picture.  The sequence, at the output of the decoding process, consists of a series of reconstructed frames that are separated in time by a frame period.

6.1.2.4	Frame

A frame consists of three rectangular matrices of integers; a luminance matrix (Y), and two chrominance matrices (Cb and Cr).

The relationship between these Y, Cb and Cr components and the primary (analogue) Red, Green and Blue Signals (E'R, E'G  and E'B), the chromaticity of these primaries and the transfer characteristics of the source frame may be specified in the bitstream (or specified by some other means).  This information does not affect the decoding process.

6.1.2.4	Field

A field consists of every other line of samples in the three rectangular matrices of integers representing a frame.

A frame is the union of a top field and a bottom field.  The top field is the field that contains the top-most line of each of the three matrices.  The bottom field is the other one.

6.1.2.4	Picture

A reconstructed picture is obtained by decoding a coded picture, i.e. a picture header, the optionnal extensions immediately following it, and the picture data.  A coded picture may be a frame picture or a field picture.  A reconstructed picture is either a reconstructed frame (when decoding a frame picture), or one field of a reconstructed frame (when decoding a field picture).

6.1.2.5.1	Field pictures

If field pictures are used then they shall occur in pairs (one top field and one bottom field) and together constitute a coded frame.  The two field pictures that comprise a coded frame shall be encoded in the bitstream in the order in which they shall occur at the output of the decoding process.

When the first picture of the coded frame is a P-field picture, then the second picture of the coded frame shall also be a P- field picture.  Similarly when the first picture of the coded frame is a B-field picture the second picture of the coded frame shall also be a B-field picture.

When the first picture of the coded frame is a I-field picture, then the second picture of the frame shall be either an I-field picture or a P-field picture.

6.1.2.5.2	Frame pictures

When coding interlaced sequences using  frame pictures, the two fields of the frame shall be interleaved with one another and then the entire frame is coded as a single frame-picture.

6.1.2.4	Picture types

There are three types of pictures that use different coding methods.

An Intra-coded (I) picture is coded using information only from itself.

A Predictive-coded (P) picture is a picture which is coded using motion compensated prediction from a past I-picture or P-picture.

A Bidirectionally predictive-coded (B) picture is a picture which is coded using motion compensated prediction from a past and/or future I-picture or P-picture.

6.1.1.2	Sequence header

A video sequence header commences with a sequence_header_code and is followed by a series of data elements.  In this specification sequence_header() shall be followed by sequence_extension() which includes further parameters beyond those used by ISO/IECÊ11172-2.  When sequence_extension() is present, the syntax and semantics defined in ISO/IECÊ11172-2 does not apply, and the present specification applies.

In repeated sequence headers all of the data elements with the permitted exception of those defining the quantisation matrices (load_intra_quantiser_matrix, load_non_intra_quantiser_matrix and optionally intra_quantiser_matrix and non_intra_quantiser_matrix) shall have the same values as in the first sequence header. The quantisation matrices may be redefined each time that a sequence header occurs in the bitstream (Note that quantisation matrices may also be updated using quant_matrix_extension()).

All of the data elements in the sequence_extension() that follows a repeat sequence_header() shall have the same values as in the first sequence_extension().

If a sequence_scalable_extension() occurs after the first sequence_header() all subsequent sequence headers shall be followed by sequence_scalable_extension() in which all data elements are the same as in the first sequence_scalable_extension().  Conversely if no sequence_scalable_extension() occurs between the first sequence_header() and the first picture_header() then sequence_scalable_extension() shall not occur in the bitstream.

If a sequence_display_extension() occurs after the first sequence_header() all subsequent sequence headers shall be followed by sequence_display_extension() in which all data elements are the same as in the first sequence_display_extension().  Conversely if no sequence_display_extension() occurs between the first sequence_header() and the first picture_header() then sequence_display_extension() shall not occur in the bitstream.

Repeating the sequence header allows the data elements of the initial sequence header to be repeated in order that random access into the video sequence is possible.

In the coded bitstream, a repeat sequence header may precede either an I-picture or a P-picture but not a B-picture. In the case that an interlaced frame is coded as two separate field pictures a repeat sequence header shall not precede the second of these two field pictures.

If a bitstream is edited so that all of the data preceding any of the repeated sequence headers is removed (or alternatively random access is made to that sequence header) then the resulting bitstream shall be a legal bitstream that complies with this specification.  In the case that the first picture of the resulting bitstream is a P-picture, it is possible that it will contain non-intra macroblocks.  Since the reference picture(s) required by the decoding process are not available, the reconstructed picture may not be fully defined.  The time taken to fully refresh the entire frame depends on the refresh techniques employed.

6.1.1.3	I-pictures and group of pictures header

I-pictures are intended to assist random access into the sequence. Applications requiring random access, fast-forward playback, or fast reverse playback may use I-pictures relatively frequently.

I-pictures may also be used at scene cuts or other cases where motion compensation is ineffective.

Group of picture header is an optional header that can be used immediately before a coded I-frame to indicate to the decoder if the first consecutive B-pictures immediately following the coded I-frame can be reconstructed properly in the case of a random access.  In effect, if the preceding reference frame is not available, those B-pictures, if any, cannot be reconstructed properly unless they only use backward prediction.  This is more precisely defined in the section describing closed_gop and broken_link.  A group of picture header also contains a time code information that is not used by the decoding process.

In the coded bitstream, the first coded frame following a group of pictures header shall be a coded I-frame.

6.1.2.1	4:2:0 Format

In this format the Cb and Cr matrices shall be one half the size of the Y-matrix in both horizontal and vertical dimensions.  The Y-matrix shall have an even number of lines and samples.

Note	When interlaced frames are coded as field pictures, the picture reconstructed from each of these field pictures shall have a Y-matrix with half the number of lines as the corresponding frame.  Thus the total number of lines in the Y-matrix of an entire frame shall be divisible by four.

The luminance and chrominance samples are positioned as shown in Figure 6-1.

In order to further specify the organisation, Figures 6-2a and 6-2b show the (vertical) positioning of the samples in an interlaced frame.  Figures 6-3 shows the (vertical) positioning of the samples in an progressive frame.

In each field of an interlaced frame, the chrominance samples do not lie (vertically) mid way between the luminance samples of the field, this is so that the spatial location of the chrominance samples in the frame is the same whether the frame is represented as a single frame-picture or two field-pictures.

Represent luminance samples

Represent chrominance samples

Figure 6-1 -- The position of luminance and chrominance samples. 4:2:0 data.

Figure 6-2a Ð Vertical  and temporal positions of samples in an interlaced frame with top_field_first = 1.

Figure 6-2b Ð Vertical and temporal positions of samples in an interlaced frame with top_field_first = 0.

Figure 6-3 Ð Vertical  and temporal positions of samples in a progressive frame.

6.1.2.2	4:2:2 Format

In this format the Cb and Cr matrices shall be one half the size of the Y-matrix in the horizontal dimension and the same size as the Y-matrix in the vertical dimension.   The Y-matrix shall have an even number of samples.

Note	When interlaced frames are coded as field pictures, the picture reconstructed from each of these field pictures shall have a Y-matrix with half the number of lines as the corresponding frame.  Thus the total number of lines in the Y-matrix of an entire frame shall be divisible by two.

The luminance and chrominance samples are positioned as shown in Figure 6-3.

In order to clarify the organisation, Figure 6-4 shows the (vertical) positioning of the samples when the frame is separated into two fields.

Represent luminance samples

Represent chrominance samples

Figure 6-3 -- The position of luminance and chrominance samples. 4:2:2 data.

Figure 6-4 Ð Vertical positions of samples with 4:2:2 and 4:4:4 data

6.1.2.3	4:4:4 Format

In this format the Cb and Cr matrices shall be the same size as the Y-matrix in the horizontal and the vertical dimensions.

Note	When interlaced frames are coded as field pictures, the picture reconstructed from each of these field pictures shall have a Y-matrix with half the number of lines as the corresponding frame.  Thus the total number of lines in the Y-matrix of an entire frame shall be divisible by two.

The luminance and chrominance samples are positioned as shown in Figures 6-4 and 6-5.

Represent luminance samples

Represent chrominance samples

Figure 6-5 -- The position of luminance and chrominance samples. 4:4:4 data.

6.1.1.1	Frame reordering

The order of the coded frames in the coded bitstream is the order in which the decoder processes them.  When B-pictures are used in a sequence, the order of the coded frames in the bitstream is sometimes different from the order at which the reconstructed frames or fields are output by the decoding process.

The following is an example of pictures taken from the beginning of a video sequence. In this example there are two coded B-frames between successive coded P-frames and also two coded B-frames between successive coded I- and P-frames and all pictures are frame-pictures. Frame '1IÕ is used to form a prediction for frame '4P'. Frames '4P' and '1I' are both used to form predictions for frames '2B' and '3B'. Therefore the order of coded frames in the coded sequence shall be '1I', '4P', '2B', '3B'. However, the decoder shall display them in the order '1I', '2B', '3B', '4P'.

At the encoder input,

1

I

2

B

3

B

4

P

5

B

6

B

7

P

8

B

9

B

10

I

11

B

12

B

13

| P |  |
| --- | --- |

At the encoder output, in the coded bitstream, and at the decoder input,

1

I

4

P

2

B

3

B

7

P

5

B

6

B

10

I

8

B

9

B

13

P

11

B

12

| B |  |
| --- | --- |

At the decoder output,

| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

The number of consecutive coded B-frames is variable.  Coded B-frames may not be present between successive coded P-frames (or between coded I-frame and coded P-frames).  Within each group of consecutive coded B-frames the frames shall occur in the bitstream in the order in which they shall appear at the decoder output.

A sequence may also contain no coded I-frame in which case some care is required at the start of the sequence and within the sequence to effect both random access and error recovery.

A sequence may contain no coded P-frame.

A sequence shall not be composed of only coded B-frames.

6.1.3	Slice

A slice is a series of an arbitrary number of macroblocks.  The first and last macroblocks of a slice shall not be skipped macroblocks.  Every slice shall contain at least one macroblock.  Slices shall not overlap.  The position of slices may change from picture to picture.

The first and last macroblock of a slice shall be in the same horizontal row of macroblocks.

Slices shall occur in the bitstream in the order in which they are encountered, starting at the upper-left of the picture and proceeding by raster-scan order from left to right and top to bottom (illustrated in the Figures of this clause as alphabetical order).

6.1.3.1	The general slice structure

In the most general case it is not necessary for the slices to cover the entire picture.  Figure 6-6 shows this case.  Those areas that are not enclosed in a slice are not encoded and no information is encoded for such areas (in the specific picture).

If the slices do not cover the entire picture then it is a requirement that if the picture is subsequently used to form predictions then predictions shall only be made from those regions of the picture that were enclosed in slices.  It is the responsibility of the encoder to ensure this.

This specification does not define what action a decoder shall take in the regions between the slices.

Figure 6-6. The most general slice structure.

6.1.3.2	Restricted slice structure

In certain defined levels of defined profiles a restricted slice structure illustrated in Figure 6-7 shall be used.  In this case every macroblock in the picture shall be enclosed in a slice.

Figure 6-7. Restricted slice structure.

Where a defined level of a defined profile requires that the slice structure obeys the restrictions detailed in this clause, the term Òrestricted slice structureÓ may be used.

6.1.4	Macroblock

A macroblock contains a section of the luminance component and the spatially corresponding chrominance components.  The term macroblock can either refer to source and decoded data or to the corresponding coded data elements. A skipped macroblock is one for which no information is transmitted (see 7.6.6).  There are three chrominance formats for a macroblock, namely, 4:2:0, 4:2:2 and 4:4:4 formats. The orders of blocks in a macroblock shall be different for each different chrominance format and are illustrated below:

A 4:2:0 Macroblock consists of 6 blocks. This structure holds 4 Y, 1 Cb and 1 Cr Blocks and the block order is depicted in Figure 6-8.

Figure 6-8  4:2:0 Macroblock structure

A 4:2:2 Macroblock consists of 8 blocks. This structure holds 4 Y, 2 Cb and 2 Cr Blocks and the block order is depicted in Figure 6-9.

Figure 6-9  4:2:2 Macroblock structure

A 4:4:4 Macroblock consists of 12 blocks. This structure holds 4 Y, 4 Cb and 4 Cr Blocks and the block order is depicted in Figure 6-10.

Figure 6-10  4:4:4 Macroblock structure

In frame pictures, where both frame and field DCT coding may be used, the internal organisation within the macroblock is different in each case.

¥	In the case of frame DCT coding, each block shall be composed of lines from the two fields alternately. This is illustrated in Figure 6-12.

¥	In the case of field DCT coding, each block shall be composed of lines from only one of the two fields. This is illustrated in Figure 6-13.

In the case of chrominance blocks the structure depends upon the chrominance format that is being used.  In the case of 4:2:2 and 4:4:4 formats (where there are two blocks in the vertical dimension of the macroblock) the chrominance blocks are treated in exactly the same manner as the luminance blocks.  However, In the 4:2:0 format the chrominance blocks shall always be organised in frame structure for the purposes of DCT coding.  It should however be noted that field based predictions may be made for these blocks which will, in the general case, require that predictions for 8x4 regions (after half-sample filtering) must be made.

In the case of a progressive frame, frame DCT coding shall always be used as illustrated in FigureÊ6-12.

In field pictures, each picture only contains lines from one of the fields.  In this case each block consists of lines taken from successive lines in the picture as illustrated by FigureÊ6-12.

Figure 6-12   Luminance macroblock structure in frame DCT coding

Figure 6-13   Luminance macroblock structure in field DCT coding

6.1.5	Block

The term "block" can refer either to source and reconstructed data or to the DCT coefficients or to the corresponding coded data elements.

When ÒblockÓ refers to source and reconstructed data it refers to an orthogonal section of a luminance or chrominance component with the same number of lines and samples.  There are 8 lines and 8 samples in the block.

6.2	Video bitstream syntax

6.2.1	Start codes

Start codes are specific bit patterns that do not otherwise occur in the video stream.

Each start code consists of a start code prefix followed by a start code value.  The start code prefix is a string of twenty three bits with the value zero followed by a single bit with the value one.  The start code prefix is thus the bit string "0000 0000 0000 0000 0000 0001".

The start code value is an eight bit integer which identifies the type of start code.  Most types of start code have just one start code value.  However slice_start_code is represented by many start code values, in this case the start code value is the slice_vertical_position for the slice.

All start codes shall be byte aligned.  This shall be achieved by inserting bits with the value zero before the start code prefix such that the first bit of the start code prefix is the most significant bit of a byte.

TableÊ6-1 defines the slice code values for the start codes used in the video bitstream.

TableÊ6-1 Ñ Start code values

name

start code value

| (hexadecimal) |  | picture_start_code | 00 |  | slice_start_code | 01 through AF |  | reserved | B0 |  | reserved | B1 |  | user_data_start_code | B2 |  | sequence_header_code | B3 |  | sequence_error_code | B4 |  | extension_start_code | B5 |  | reserved | B6 |  | sequence_end_code | B7 |  | group_start_code | B8 |  | system start codes (see note) | B9 through FF |  | NOTE - system start codes are defined in Part 1 of this specification |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

The use of the start codes is defined in the following syntax description with the exception of the sequence_error_code. The sequence_error_code has been allocated for use by a media interface to indicate where uncorrectable errors have been detected.

6.2.2	Video Sequence

| video_sequence() { | No. of bits | Mnemonic |  | next_start_code() |  |  |  | sequence_header() |  |  |  | if ( nextbits() == extension_start_code ) { |  |  |  | sequence_extension() |  |  |  | do { |  |  |  | extension_and_user_data( 0 ) |  |  |  | do { |  |  |  | if (nextbits() == group_start_code) { |  |  |  | group_of_pictures_header() |  |  |  | extension_and_user_data( 1 ) |  |  |  | } |  |  |  | picture_header() |  |  |  | picture_coding_extension() |  |  |  | extensions_and_user_data( 2 ) |  |  |  | picture_data() |  |  |  | } while ( (nextbits() == picture_start_code) ¦¦ |  |  |  | (nextbits() == group_start_code) ) |  |  |  | if ( nextbits() != sequence_end_code ) { |  |  |  | sequence_header() |  |  |  | sequence_extension() |  |  |  | } |  |  |  | } while ( nextbits() != sequence_end_code ) |  |  |  | } else { |  |  |  | /* ISO/IEC 11172-2 */ |  |  |  | } |  |  |  | sequence_end_code | 32 | bslbf |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.2.1	Sequence header

| sequence_header() { | No. of bits | Mnemonic |  | sequence_header_code | 32 | bslbf |  | horizontal_size_value | 12 | uimsbf |  | vertical_size_value | 12 | uimsbf |  | aspect_ratio_information | 4 | uimsbf |  | frame_rate_code | 4 | uimsbf |  | bit_rate_value | 18 | uimsbf |  | marker_bit | 1 | bslbf |  | vbv_buffer_size_value | 10 | uimsbf |  | constrained_parameters_flag | 1 |  |  | load_intra_quantiser_matrix | 1 |  |  | if ( load_intra_quantiser_matrix ) |  |  |  | intra_quantiser_matrix[64] | 8*64 | uimsbf |  | load_non_intra_quantiser_matrix | 1 |  |  | if ( load_non_intra_quantiser_matrix ) |  |  |  | non_intra_quantiser_matrix[64] | 8*64 | uimsbf |  | next_start_code() |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.2.2	Extension and user data

| extension_and_user_data( i ) { | No. of bits | Mnemonic |  | while ( ( nextbits()== extension_start_code ) ¦¦ |  |  |  | ( nextbits()== user_data_start_code ) ) { |  |  |  | if ( i != 1 ) |  |  |  | if ( nextbits()== extension_start_code ) |  |  |  | extension_data( i ) |  |  |  | if ( nextbits()== user_data_start_code ) |  |  |  | user_data() |  |  |  | } |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.2.2.1	Extension data

| extension_data( i ) { | No. of bits | Mnemonic |  | while ( nextbits()== extension_start_code ) { |  |  |  | extension_start_code | 32 | bslbf |  | if (i == 0) { /* follows sequence_extension() */ |  |  |  | if ( nextbits()== ÒSequence Display Extension IDÓ ) |  |  |  | sequence_display_extension() |  |  |  | if ( nextbits()== ÒSequence Scalable Extension IDÓ ) |  |  |  | sequence_scalable_extension() |  |  |  | } |  |  |  | /* Note: extension never follows a group_of_pictures_header() */ |  |  |  | if (i == 2) { /* follows picture_coding_extension() */ |  |  |  | if ( nextbits()== ÒQuant Matrix Extension IDÓ ) |  |  |  | quant_matrix_extension() |  |  |  | if ( nextbits()== ÒPicture Pan Scan Extension IDÓ ) |  |  |  | picture_display_extension() |  |  |  | if ( nextbits()== ÒPicture Spatial Scalable Extension IDÓ ) |  |  |  | picture_spatial_scalable_extension() |  |  |  | if ( nextbits()== ÒPicture Temporal Scalable Ext. IDÓ ) |  |  |  | picture_temporal_scalable_extension() |  |  |  | } |  |  |  | } |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.2.2.2	User data

| user_data() { | No. of bits | Mnemonic |  | user_data_start_code | 32 | bslbf |  | while( nextbits() != Ô0000 0000 0000 0000 0000 0001Õ ) { |  |  |  | user_data | 8 |  |  | } |  |  |  | next_start_code() |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.2.3	Sequence extension

| sequence_extension() { | No. of bits | Mnemonic |  | extension_start_code | 32 | bslbf |  | extension_start_code_identifier | 4 | uimsbf |  | profile_and_level_indication | 8 | uimsbf |  | progressive_sequence | 1 | uimsbf |  | chroma_format | 2 | uimsbf |  | horizontal_size_extension | 2 | uimsbf |  | vertical_size_extension | 2 | uimsbf |  | bit_rate_extension | 12 | uimsbf |  | marker_bit | 1 | bslbf |  | vbv_buffer_size_extension | 8 | uimsbf |  | low_delay | 1 | uimsbf |  | frame_rate_extension_n | 2 | uimsbf |  | frame_rate_extension_d | 5 | uimsbf |  | next_start_code() |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.2.4	Sequence display extension

| sequence_display_extension() { | No. of bits | Mnemonic |  | extension_start_code_identifier | 4 | uimsbf |  | video_format | 3 | uimsbf |  | colour_description | 1 | uimsbf |  | if ( colour_description ) { |  |  |  | colour_primaries | 8 | uimsbf |  | transfer_characteristics | 8 | uimsbf |  | matrix_coefficients | 8 | uimsbf |  | } |  |  |  | display_horizontal_size | 14 | uimsbf |  | marker_bit | 1 | bslbf |  | display_vertical_size | 14 | uimsbf |  | next_start_code() |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.2.5	Sequence scalable extension

| sequence_scalable_extension() { | No. of bits | Mnemonic |  | extension_start_code_identifier | 4 | uimsbf |  | scalable_mode | 2 | uimsbf |  | layer_id | 4 | uimsbf |  | if (scalable_mode == Òspatial scalabilityÓ) { |  |  |  | lower_layer_prediction_horizontal_size | 14 | uimsbf |  | marker_bit | 1 | bslbf |  | lower_layer_prediction_vertical_size | 14 | uimsbf |  | horizontal_subsampling_factor_m | 5 | uimsbf |  | horizontal_subsampling_factor_n | 5 | uimsbf |  | vertical_subsampling_factor_m | 5 | uimsbf |  | vertical_subsampling_factor_n | 5 | uimsbf |  | } |  |  |  | if ( scalable_mode == Òtemporal scalabilityÓ ) { |  |  |  | picture_mux_enable | 1 | uimsbf |  | if ( picture_mux_enable ) |  |  |  | mux_to_progressive_sequence | 1 | uimsbf |  | picture_mux_order | 3 | uimsbf |  | picture_mux_factor | 3 | uimsbf |  | } |  |  |  | next_start_code() |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.2.6	Group of pictures header

| group_of_pictures_header() { | No. of bits | Mnemonic |  | group_start_code | 32 | bslbf |  | time_code | 25 | bslbf |  | closed_gop | 1 | uimsbf |  | broken_link | 1 | uimsbf |  | next_start_code() |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.3	Picture header

| picture_header() { | No. of bits | Mnemonic |  | picture_start_code | 32 | bslbf |  | temporal_reference | 10 | uimsbf |  | picture_coding_type | 3 | uimsbf |  | vbv_delay | 16 | uimsbf |  | if ( picture_coding_type == 2 ¦¦ picture_coding_type == 3) { |  |  |  | full_pel_forward_vector | 1 |  |  | forward_f_code | 3 | uimsbf |  | } |  |  |  | if ( picture_coding_type == 3 ) { |  |  |  | full_pel_backward_vector | 1 |  |  | backward_f_code | 3 | uimsbf |  | } |  |  |  | while ( nextbits() == '1' ) { |  |  |  | extra_bit_picture /* with the value Ò1Ó */ | 1 | uimsbf |  | extra_information_picture | 8 |  |  | } |  |  |  | extra_bit_picture /* with the value Ò0Ó */ | 1 | uimsbf |  | next_start_code() |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.3.1	Picture coding extension

| picture_coding_extension() { | No . of bits | Mnemonic |  | extension_start_code | 32 | bslbf |  | extension_start_code_identifier | 4 | uimsbf |  | f_code[0][0] /* forward horizontal */ | 4 | uimsbf |  | f_code[0][1] /* forward vertical */ | 4 | uimsbf |  | f_code[1][0] /* backward horizontal */ | 4 | uimsbf |  | f_code[1][1] /* backward vertical */ | 4 | uimsbf |  | intra_dc_precision | 2 | uimsbf |  | picture_structure | 2 | uimsbf |  | top_field_first | 1 | uimsbf |  | frame_pred_frame_dct | 1 | uimsbf |  | concealment_motion_vectors | 1 | uimsbf |  | q_scale_type | 1 | uimsbf |  | intra_vlc_format | 1 | uimsbf |  | alternate_scan | 1 | uimsbf |  | repeat_first_field | 1 | uimsbf |  | chroma_420_type | 1 | uimsbf |  | progressive_frame | 1 | uimsbf |  | composite_display_flag | 1 | uimsbf |  | if ( composite_display_flag ) { |  |  |  | v_axis | 1 | uimsbf |  | field_sequence | 3 | uimsbf |  | sub_carrier | 1 | uimsbf |  | burst_amplitude | 7 | uimsbf |  | sub_carrier_phase | 8 | uimsbf |  | } |  |  |  | next_start_code() |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.3.2	Quant matrix extension

| quant_matrix_extension() { | No. of bits | Mnemonic |  | extension_start_code_identifier | 4 | uimsbf |  | load_intra_quantiser_matrix | 1 | uimsbf |  | if ( load_intra_quantiser_matrix ) |  |  |  | intra_quantiser_matrix[64] | 8 * 64 | uimsbf |  | load_non_intra_quantiser_matrix | 1 | uimsbf |  | if ( load_non_intra_quantiser_matrix ) |  |  |  | non_intra_quantiser_matrix[64] | 8 * 64 | uimsbf |  | load_chroma_intra_quantiser_matrix | 1 | uimsbf |  | if ( load_chroma_intra_quantiser_matrix ) |  |  |  | chroma_intra_quantiser_matrix[64] | 8 * 64 | uimsbf |  | load_chroma_non_intra_quantiser_matrix | 1 | uimsbf |  | if ( load_chroma_non_intra_quantiser_matrix ) |  |  |  | chroma_non_intra_quantiser_matrix[64] | 8 * 64 | uimsbf |  | next_start_code() |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.3.3	Picture display extension

| picture_display_extension() { | No. of bits | Mnemonic |  | extension_start_code_identifier | 4 | uimsbf |  | for ( i=0; i<number_of_frame_centre_offsets; i++ ) { |  |  |  | frame_centre_horizontal_offset | 16 | simsbf |  | marker_bit | 1 | bslbf |  | frame_centre_vertical_offset | 16 | simsbf |  | marker_bit | 1 | bslbf |  | } |  |  |  | next_start_code() |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.3.4	Picture temporal scalable extension

| picture_temporal_scalable_extension() { | No. of bits | Mnemonic |  | extension_start_code_identifier | 4 | uimsbf |  | reference_select_code | 2 | uimsbf |  | forward_temporal_reference | 10 | uimsbf |  | marker_bit | 1 | bslbf |  | backward_temporal_reference | 10 | uimsbf |  | next_start_code() |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.3.5	Picture spatial scalable extension

| picture_spatial_scalable_extension() { | No. of bits | Mnemonic |  | extension_start_code_identifier | 4 | uimsbf |  | lower_layer_temporal_reference | 10 | uimsbf |  | marker_bit | 1 | bslbf |  | lower_layer_horizontal_offset | 15 | simsbf |  | marker_bit | 1 | bslbf |  | lower_layer_vertical_offset | 15 | simsbf |  | spatial_temporal_weight_code_table_index | 2 | uimsbf |  | lower_layer_progressive_frame | 1 | uimsbf |  | lower_layer_deinterlaced_field_select | 1 | uimsbf |  | next_start_code() |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.3.6	Picture data

| picture_data() { | No. of bits | Mnemonic |  | do { |  |  |  | slice() |  |  |  | } while ( nextbits() == slice_start_code ) |  |  |  | next_start_code() |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.4	Slice

| slice() { | No. of bits | Mnemonic |  | slice_start_code | 32 | bslbf |  | if (vertical_size > 2800) |  |  |  | slice_vertical_position_extension | 3 | uimsbf |  | if ( <sequence_scalable_extension() is present in the bitstream> ) |  |  |  | if (scalable_mode == Òdata partitioningÓ ) |  |  |  | priority_breakpoint | 7 | uimsbf |  | quantiser_scale_code | 5 | uimsbf |  | if ( nextbits() == '1' ) { |  |  |  | intra_slice_flag | 1 | bslbf |  | intra_slice | 1 | uimsbf |  | reserved_bits | 7 | uimsbf |  | while ( nextbits() == '1' ) { |  |  |  | extra_bit_slice /* with the value Ò1Ó */ | 1 | uimsbf |  | extra_information_slice | 8 |  |  | } |  |  |  | } |  |  |  | extra_bit_slice /* with the value Ò0Ó */ | 1 | uimsbf |  | do { |  |  |  | macroblock() |  |  |  | } while ( nextbits() != '000Ê0000Ê0000Ê0000Ê0000Ê0000' ) |  |  |  | next_start_code() |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.5	Macroblock

| macroblock() { | No. of bits | Mnemonic |  | while ( nextbits() == '0000 0001 000' ) |  |  |  | macroblock_escape | 11 | bslbf |  | macroblock_address_increment | 1-11 | vlclbf |  | macroblock_modes() |  |  |  | if ( macroblock_quant ) |  |  |  | quantiser_scale_code | 5 | uimsbf |  | if ( macroblock_motion_forward ¦¦ |  |  |  | ( macroblock_intra && concealment_motion_vectors) ) |  |  |  | motion_vectors( 0 ) |  |  |  | if ( macroblock_motion_backward ) |  |  |  | motion_vectors( 1 ) |  |  |  | if ( macroblock_intra && concealment_motion_vectors) |  |  |  | marker_bit | 1 | bslbf |  | if ( macroblock_pattern ) |  |  |  | coded_block_pattern() |  |  |  | for ( i=0; i<block_count; i++ ) { |  |  |  | block( i ) |  |  |  | } |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.5.1	Macroblock modes

| macroblock_modes() { | No. of bits | Mnemonic |  | macroblock_type | 1-9 | vlclbf |  | if ( ( spatial_temporal_weight_code_flag == 1 ) && |  |  |  | ( spatial_temporal_weight_code_table_index != Ô00Õ) ) { |  |  |  | spatial_temporal_weight_code | 2 | uimsbf |  | } |  |  |  | if ( macroblock_motion_forward ¦¦ |  |  |  | macroblock_motion_backward ) { |  |  |  | if ( picture_structure == ÔframeÕ ) { |  |  |  | if ( frame_pred_frame_dct == 0 ) |  |  |  | frame_motion_type | 2 | uimsbf |  | } else { |  |  |  | field_motion_type | 2 | uimsbf |  | } |  |  |  | } |  |  |  | if ( decode_dct_type ) { |  |  |  | dct_type | 1 | uimsbf |  | } |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.5.2	Motion vectors

| motion_vectors ( s ) { | No. of bits | Mnemonic |  | if ( motion_vector_count == 1 ) { |  |  |  | if (( mv_format == field ) && ( dmv != 1)) |  |  |  | motion_vertical_field_select[0][s] | 1 | uimsbf |  | motion_vector( 0, s ) |  |  |  | } else { |  |  |  | motion_vertical_field_select[0][s] | 1 | uimsbf |  | motion_vector( 0, s ) |  |  |  | motion_vertical_field_select[1][s] | 1 | uimsbf |  | motion_vector(1, s ) |  |  |  | } |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.5.2.1	Motion vector

| motion_vector ( r, s ) { | No. of bits | Mnemonic |  | motion_code[r][s][0] | 1-11 | vlclbf |  | if ( ( f_code[s][0] != 1) && ( motion_code[r][s][0] != 0 ) ) |  |  |  | motion_residual[r][s][0] | 1-8 | uimsbf |  | if (dmv == 1) |  |  |  | dmvector[0] | 1-2 | vlclbf |  | motion_code[r][s][1] | 1-11 | vlclbf |  | if ( ( f_code[s][0] != 1) && ( motion_code[r][s][1] != 0 ) ) |  |  |  | motion_residual[r][s][1] | 1-8 | uimsbf |  | if (dmv == 1) |  |  |  | dmvector[1] | 1-2 | vlclbf |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.5.3	Coded block pattern

| coded_block_pattern () { | No. of bits | Mnemonic |  | coded_block_pattern_420 | 3-9 | vlclbf |  | if ( chroma_format == 4:2:2 ) |  |  |  | coded_block_pattern_1 | 2 | uimsbf |  | if ( chroma_format == 4:4:4 ) |  |  |  | coded_block_pattern_2 | 6 | uimsbf |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.2.6	Block

The detailed syntax for the terms ÒFirst DCT coefficientÓ, ÒSubsequent DCT coefficientÓ and ÒEnd of BlockÓ is fully described in 7.2.

Note	This clause does not adequately document the block layer syntax when data partitioning is used.  See 7.10.

| block( i ) { | No. of bits | Mnemonic |  | if ( pattern_code[i] ) { |  |  |  | if ( macroblock_intra ) { |  |  |  | if ( i<4 ) { |  |  |  | dct_dc_size_luminance | 2-9 | vlclbf |  | if(dct_dc_size_luminance != 0) |  |  |  | dct_dc_differential | 1-11 | uimsbf |  | } else { |  |  |  | dct_dc_size_chrominance | 2-10 | vlclbf |  | if(dct_dc_size_chrominance !=0) |  |  |  | dct_dc_differential | 1-11 | uimsbf |  | } |  |  |  | } else { |  |  |  | First DCT coefficient |  |  |  | } |  |  |  | while ( nextbits() != End of block ) |  |  |  | Subsequent DCT coefficients |  |  |  | End of block |  |  |  | } |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.3	Video bitstream semantics

6.3.1	Semantic rules for higher syntactic structures

This clause details the rules that govern the way in which the higher level syntactic elements may be combined together to produce a legal bitstream.  Subsequent clauses detail the semantic meaning of all fields in the video bitstream.

Figure 6-14 illustrates the high level structure of the video bitstream.

The following semantic rules apply:

¥	If the first sequence_header() of the sequence is not followed by sequence_extension() then the stream shall conform to ISO/IEC 11172-2 and is not documented within this specification.

¥	If the first sequence_header() of a sequence is followed by a sequence_extension() then all subsequent occurrences of sequence_header() shall also be immediately followed by a sequence_extension().

¥	sequence_extension() shall only occur immediately following a sequence_header().

¥	If sequence_extension() occurs in the bitstream then each picture_header() shall be followed immediately by a picture_coding_extension().

¥	picture_coding_extension() shall only occur immediately following a picture_header().

¥	The first coded picture following a group_of_pictures_header() shall be an I-picture.

A number of different extensions are defined in addition to sequence_extension() and picture_coding_extension().  The set of allowed extensions is different at each different point in the syntax where extensions are allowed.  TableÊ6-2 defines a four bit extension_start_code_identifier for each extension.

At each point where extensions are allowed in the bitstream any number of the extensions from the defined allowable set may be included.  However each type of extension shall not occur more than once.

In the case that a decoder encounters an extension with an extension identification that is described as ÒreservedÓ in this specification the decoder shall discard all subsequent data until the next start code.  This requirement allows future definition of compatible extensions to this specification.

Figure 6-14. High level bitstream organisation

TableÊ6-2. extension_start_code_identifier codes.

| extension_start_code_identifier | Name |  | 0000 | reserved |  | 0001 | Sequence Extension ID |  | 0010 | Sequence Display Extension ID |  | 0011 | Quant Matrix Extension ID |  | 0100 | reserved |  | 0101 | Sequence Scalable Extension ID |  | 0110 | reserved |  | 0111 | Picture Display Extension ID |  | 1000 | Picture Coding Extension ID |  | 1001 | Picture Spatial Scalable Extension ID |  | 1010 | Picture Temporal Scalable Extension ID |  | 1011 | reserved |  | 1100 | reserved |  | ... | ... |  | 1111 | reserved |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.3.2	Video sequence

sequence_end_code -- The sequence_end_code is the bit string 000001B7 in hexadecimal. It terminates a video sequence.

6.3.3	Sequence header

sequence_header_code -- The sequence_header_code is the bit string 000001B3 in hexadecimal. It identifies the beginning of a sequence header.

horizontal_size_value -- This word forms the 12 least significant bits of horizontal_size.

vertical_size_value -- This word forms the 12 least significant bits of vertical_size.

horizontal_size -- The horizontal_size is a 14-bit unsigned integer, the 12 least significant bits are defined in horizontal_size_value, the 2 most significant bits are defined in horizontal_size_extension. The horizontal_size_value is the width of the displayable part of the luminance component of pictures in samples. The width of the encoded luminance component of pictures in macroblocks, mb_width, is (horizontal_sizeÊ+Ê15)/16. The displayable part is left-aligned in the encoded pictures.

In order to avoid start code emulation horizontal_size_value shall not be zero.  This precludes values of horizontal_size that are multiples of 4096.

vertical_size -- The vertical_size is a 14-bit unsigned integer, the 12 least significant bits are defined in vertical_size_value, the 2 most significant bits are defined in vertical_size_extension. The vertical_size_value is the height of the displayable part of the luminance component of the frame in lines.

In the case that progressive_sequence is Ò1Ó the height of the encoded luminance component of pictures in macroblocks, mb_height, is (vertical_sizeÊ+Ê15)/16.

In the case that progressive_sequence is Ò0Ó the height of the encoded luminance component of pictures in macroblocks, mb_height, is 2*((vertical_sizeÊ+Ê31)/32). The height of the encoded luminance component of field pictures in macroblocks, mb_height, is ((vertical_sizeÊ+Ê31)/32).

The displayable part is top-aligned in the encoded pictures.

In order to avoid start code emulation vertical_size_value shall not be zero.  This precludes values of vertical_size that are multiples of 4096.

aspect_ratio_information -- This is a four-bit integer defined in the TableÊ6-3.

aspect_ratio_information either specifies that the Òsample aspect ratioÓ (SAR) of the reconstructed frame is 1,0 (square samples) or alternatively it gives the Òdisplay aspect ratioÓ (DAR).

¥	If sequence_display_extension() is not present then it is intended that the entire reconstructed frame is intended to be mapped to the entire active region of the display.  The sample aspect ratio may be calculated as follows:

Note	In this case horizontal_size and vertical_size are constrained by the SAR of the source and the DAR selected.

¥	If sequence_display_extension() is present then the sample aspect ratio may be calculated as follows:

TableÊ6-3. aspect_ratio_information

| aspect_ratio_information | Sample Aspect Ratio | DAR |  | 0000 | forbidden | forbidden |  | 0001 | 1,0 (Square Sample) | - |  | 0010 | - | 3Ö4 |  | 0011 | - | 9Ö16 |  | 0100 | - | 1Ö2,21 |  | 0101 | - | reserved |  | ... |  | ... |  | 1111 | - | reserved |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

frame_rate_code -- This is a four-bit integer used to define frame_rate_value as shown in TableÊ6-4.  frame_rate may be derived from frame_rate_value, frame_rate_extension_n and frame_rate_extension_d as follows;

frame_rate = frame_rate_value * (frame_rate_extension_n + 1) Ö (frame_rate_extension_d + 1)

When an entry for the frame rate exists directly in TableÊ6-4, frame_rate_extension_n and frame_rate_extension_d shall be zero.

If progressive_sequence is Ò1Ó the period between two successive frames at the output of the decoding process is the reciprocal of the frame_rate. See  Figure 6-15.

If progressive_sequence is Ò0Ó the period between two successive fields at the output of the decoding process is half of the reciprocal of the frame_rate. See  Figure 6-16.

The frame_rate signalled in the enhancement layer of  temporal scalability is the combined frame rate after the temporal remultiplex operation if picture_mux_enable in the sequence_scalable_extension() is set to '1'.

TableÊ6-4 --- frame_rate_value

| frame_rate_code | frame_rate_value |  | 0000 | forbidden |  | 0001 | 24Ê000Ö1001 (23,976) |  | 0010 | 24 |  | 0011 | 25 |  | 0100 | 30Ê000Ö1001 (29,97) |  | 0101 | 30 |  | 0110 | 50 |  | 0111 | 60Ê000Ö1001 (59,94) |  | 1000 | 60 |  | . . . | reserved |  | 1111 | reserved |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

bit_rate_value -- The lower 18 bits of bit_rate.

bit_rate -- This is a 30-bit integer.  The lower 18 bits of the integer are in bit_rate_value and the upper 12 bits are in bit_rate_extension.  The 30-bit integer specifies the bitrate of the bitstream measured in units of 400 bits/second, rounded upwards. The value zero is forbidden.

If the bitstream is a constant bitrate stream, the bitrate specified is the actual rate of operation of the VBV specified in annex C.  If the bitstream is a variable bitrate stream, the STD specifications in ISO/IEC 13818-1 supersede the VBV, and the bitrate specified here is used to dimension the transport stream STD (2.4.2 in ITU-TÊRec.ÊxxxÊ|ÊISO/IEC 13818-1), or the program stream STD (2.4.5 in ITU-TÊRec.ÊxxxÊ|ÊISO/IEC 13818-1).

If the bitstream is not a constant rate bitstream the vbv_delay field shall have the value FFFF in hexadecimal.

Given the value encoded in the bitrate field, the bitstream shall be generated so that the video encoding and the worst case multiplex jitter do not cause STD buffer overflow or underflow.

marker_bit -- This is one bit that shall be set to "1". This bit prevents emulation of start codes.

vbv_buffer_size_value -- the lower 10 bits of vbv_buffer_size.

vbv_buffer_size -- vbv_buffer_size is an 18-bit integer.  The lower 10 bits of the integer are in vbv_buffer_size_value  and the upper 8 bits are in vbv_buffer_size_extension.  The integer defines the size of the VBV (Video Buffering Verifier, see Annex C) buffer needed to decode the sequence. It is defined as:

B = 16 * 1024 * vbv_buffer_size

where B is the minimum VBV buffer size in bits required to decode the sequence (see Annex C).

constrained_parameters_flag  -- This flag (used in ISO/IEC 11172-2) has no meaning in this specification and shall have the value Ò0Ó.

load_intra_quantiser_matrix -- See 6.3.7 ÒQuant matrix extensionÓ

intra_quantiser_matrix -- See 6.3.7 ÒQuant matrix extensionÓ

load_non_intra_quantiser_matrix -- See 6.3.7 ÒQuant matrix extensionÓ

non_intra_quantiser_matrix -- See 6.3.7 ÒQuant matrix extensionÓ

6.3.4	Extension and user data

extension_start_code -- The extension_start_code is the bit string 000001B5 in hexadecimal. It identifies the beginning of extensions beyond ISO/IECÊ11172-2.

6.3.4.1	User data

user_data_start_code -- The user_data_start_code is the bit string 000001B2 in hexadecimal. It identifies the beginning of user data. The user data continues until receipt of another start code.

user_data -- The user_data is defined by the users for their specific applications. The user_data shall not contain a string of 23 or more zero bits.

6.3.5	Sequence extension

extension_start_code_identifier -- This is an 4-bit integer which identifies the extension. See Table 6-2.

profile_and_level_indication Ð This is an 8-bit integer used to signal the profile and level identification. The meaning of the bits is given in clauseÊ 8.

Note	In a scalable hierarchy the bitstreams of each layer may set profile_and_level_indication to a different value as specified in clauseÊ 8.

progressive_sequence Ð When set to Ò1Ó the coded video sequence contains only progressive frame-pictures.  When progressive_sequence is set to Ò0Ó the coded video sequence may contain both frame-pictures and field-pictures, and frame-picture may be progressive or interlaced frames.

chroma_format - This is a two bit integer indicating the chrominance format as defined in the TableÊ6-5.

TableÊ6-5. Meaning of chroma_format

| chroma_format | Meaning |  | 00 | reserved |  | 01 | 4:2:0 |  | 10 | 4:2:2 |  | 11 | 4:4:4 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

horizontal_size_extension -- This word forms the 2 most significant bits from horizontal_size.

vertical_size_extension -- This word forms the 2 most significant bits from vertical_size.

bit_rate_extension -- This word forms the 12 most significant bits from bit_rate.

vbv_buffer_size_extension -- This word forms the 8 most significant bits from vbv_buffer_size.

low_delay - This flag, when set to Ò1Ó, indicates that the sequence does not contain any B-pictures, that the frame reordering delay is not present in the VBV description and that VBV buffer underflow may occur.

When set to Ò0Ó, it indicates that the sequence may contain B-pictures, that the frame reordering delay is present in the VBV description and that VBV buffer underflow shall not occur.

This flag is not used during the decoding process and therefore can be ignored by decoders, but it is necessary to define and verify the compliance of low-delay bitstreams.

frame_rate_extension_n -- See frame_rate_code.

frame_rate_extension_d -- See frame_rate_code.

6.3.6	Sequence display extension

This specification does not define the display process. The information in this extension does not affect the decoding process and may be ignored by decoders that conform to this specification.

video_format - This is a three bit integer indicating the representation of the pictures before being coded in accordance with this specification.  Its meaning is defined in TableÊ6-6

TableÊ6-6. Meaning of video_format

| video_format | Meaning |  | 000 | component |  | 001 | PAL |  | 010 | NTSC |  | 011 | SECAM |  | 100 | MAC |  | 101 | Unspecified video format |  | 110 | reserved |  | 111 | reserved |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

colour_description -- A flag which if set to Ò1Ó indicates the presence of colour_primaries, transfer_characteristics and matrix_coefficients in the bitstream.

colour_primaries -- This 8-bit integer describes the chromaticity coordinates of the source primaries, and is defined in TableÊ6-7.

TableÊ6-7. Colour Primaries

| Value | Primaries |  | 0 | (forbidden) |  | 1 |
| --- | --- | --- | --- | --- | --- | --- |

ITU-R Recommendation 709 (1990)

primary	x	y

green		0,300	0,600

blue		0,150	0,060

red		0,640	0,330

| white D65 0,3127 0,3290 |  | 2 |
| --- | --- | --- |

Unspecified Video

| Image characteristics are unknown. |  | 3 | reserved |  | 4 |
| --- | --- | --- | --- | --- | --- |

ITU-R Recommendation 624-4 System M

primary	x	y

green		0,21	0,71

blue		0,14	0,08

red		0,67	0,33

| white C 0,310 0,316 |  | 5 |
| --- | --- | --- |

ITU-R Recommendation 624-4 System B, G

primary	x	y

green		0,29	0,60

blue		0,15	0,06

red		0,64	0,33

| white D65 0,313 0,329 |  | 6 |
| --- | --- | --- |

SMPTE 170M

primary	x	y

green		0,310	0,595

blue		0,155	0,070

red		0,630	0,340

| white D65 0,3127 0,3290 |  | 7 |
| --- | --- | --- |

SMPTE 240M (1987)

primary	x	y

green		0,310	0,595

blue		0,155	0,070

red		0,630	0,340

| white D65 0,3127 0,3291 |  | 8-255 | reserved |  |
| --- | --- | --- | --- | --- |

In the case that sequence_display_extension() is not present in the bitstream or colour_description is zero the chromaticity is assumed to be that corresponding to colour_primaries having the value 1.

transfer_characteristics -- This 8-bit integer describes the opto-electronic transfer characteristic of the source picture, and is defined in TableÊ6-8.

TableÊ6-8. Transfer Characteristics

| Value | Transfer Characteristic |  | 0 | (forbidden) |  | 1 |
| --- | --- | --- | --- | --- | --- | --- |

ITU-R Recommendation 709 (1990)

V = 1,099 Lc0,45 - 0,099

for 1³ Lc ³ 0,018

V = 4,500 Lc

| for 0,018> Lc ³ 0 |  | 2 |
| --- | --- | --- |

Unspecified Video

| Image characteristics are unknown. |  | 3 | reserved |  | 4 |
| --- | --- | --- | --- | --- | --- |

ITU-R Recommendation 624-4 System M

| Assumed display gamma 2,2 |  | 5 |
| --- | --- | --- |

ITU-R Recommendation 624-4 System B, G

| Assumed display gamma 2,8 |  | 6 |
| --- | --- | --- |

SMPTE 170M

V = 1,099 Lc0,45 - 0,099

for 1³ Lc ³ 0,018

V = 4,500 Lc

| for 0,018> Lc ³ 0 |  | 7 |
| --- | --- | --- |

SMPTE 240M (1987)

V = 1,1115 Lc0,45 - 0,1115

for Lc ³ 0,0228

V = 4,0 Lc

| for 0,0228> Lc |  | 8 |
| --- | --- | --- |

Linear transfer characteristics

| i.e. V = Lc |  | 9-255 | reserved |  |
| --- | --- | --- | --- | --- |

In the case that sequence_display_extension() is not present in the bitstream or colour_description is zero the transfer characteristics are assumed to be those corresponding to transfer_characteristics having the value 1.

matrix_coefficients -- This 8-bit integer describes the matrix coefficients used in deriving luminance and chrominance signals from the green, blue, and red primaries, and is defined in TableÊ6-9.

In this table;

EÕY is analogue with values between the values 0 and 1

EÕPB and EÕPR  are analogue between the values -0,5 and 0,5

EÕY is analogue between the values 0 and 1

Y, Cb and Cr are related to EÕY, EÕPB and EÕPR by the following formulae.

Y = ( 219 * EÕY ) + 16.

Cb = ( 224 * EÕPB ) + 128.

Cr = ( 224 * EÕPR ) + 128.

Note	The decoding process given by this specification limits output sample values to the range [0:255].  Thus code words outside the range implied by the above equations may occasionally occur at the output of the decoding process. In particula the code words 0 and 255 may occur.

TableÊ6-9. Matrix Coefficients

| Value | Matrix |  | 0 | (forbidden) |  | 1 |
| --- | --- | --- | --- | --- | --- | --- |

ITU-R Recommendation 709 (1990).

E¢Y = 0,7154 E¢G + 0,0721 E¢B + 0,2125 E¢R

E¢PB = -0,386 E¢G + 0,500 E¢B -0,115 E¢R

| E¢PR = -0,454 E¢G - 0,046 E¢B + 0,500 E¢R |  | 2 |
| --- | --- | --- |

Unspecified Video

| Image characteristics are unknown. |  | 3 | reserved |  | 4 |
| --- | --- | --- | --- | --- | --- |

FCC

E¢Y = 0,59 E¢G + 0,11 E¢B + 0,30 E¢R

E¢PB = -0,331 E¢G + 0,500 E¢B -0,169 E¢R

| E¢PR = -0,421 E¢G - 0,079 E¢B + 0,500 E¢R |  | 5 |
| --- | --- | --- |

ITU-R Recommendation 624-4 System B, G

E¢Y = 0,587 E¢G + 0,114 E¢B + 0,299 E¢R

E¢PB = -0,331 E¢G + 0,500 E¢B -0,169 E¢R

| E¢PR = -0,419 E¢G - 0,081 E¢B + 0,500 E¢R |  | 6 |
| --- | --- | --- |

SMPTE 170M

E¢Y = 0,587 E¢G + 0,114 E¢B + 0,299 E¢R

E¢PB = -0,331 E¢G + 0,500 E¢B -0,169 E¢R

| E¢PR = -0,419 E¢G - 0,081 E¢B + 0,500 E¢R |  | 7 |
| --- | --- | --- |

SMPTE 240M (1987)

E¢Y = 0,701 E¢G + 0,087 E¢B + 0,212 E¢R

E¢PB = -0,384 E¢G + 0,500 E¢B -0,116 E¢R

| E¢PR = -0,445 E¢G - 0,055 E¢B + 0,500 E¢R |  | 8-255 | reserved |  |
| --- | --- | --- | --- | --- |

In the case that sequence_display_extension() is not present in the bitstream or colour_description is zero the matrix coefficients are assumed to be those corresponding to matrix_coefficients having the value 1.

display_horizontal_size - See display_vertical_size.

display_vertical_size - display_horizontal_size and display_vertical_size together define a rectangle which may be considered as the Òintended displayÕsÓ active region.  If this rectangle is smaller than the encoded frame size then the display process may be expected to display only a portion of the encoded frame.  Conversely if the display rectangle is larger than the encoded frame size then the display process may be expected to display the reconstructed frames on a portion of the display device rather than on the whole display device.

display_horizontal_size shall be in the same units as horizontal_size (samples of the encoded frames).

display_vertical_size shall be in the same units as vertical_size (lines of the encoded frames).

display_horizontal_size and display_vertical_size do not affect the decoding process but may be used by the display process that is not standardised in this specification.

6.3.8	Sequence scalable extension

It is a semantic restriction that if a sequence_scalable_extension() is present in the bitstream following a given sequence_extension() then sequence_scalable_extension() shall follow every other occurrence of sequence_extension().  Thus a bitstream is either scalable or it is not scalable.  It is not possible to mix scalable and non-scalable coding within a sequence.

scalable_mode - The scalable_mode indicates the type of scalability used in the video sequence. If no sequence_scalable_extension() is present in the bitstream then no scalability is used for that sequence. scalable_mode also indicates the macroblock_type tables to be used.  However in the case of spatial scalability if no picture_spatial_scalable_extension() is present for a given picture then that picture shall be decoded in a non-scalable manner (i.e. as if sequence_scalable_extension() had not been present).

TableÊ6-10. Definition of scalable_mode

| scalable_mode | Meaning |
| --- | --- |

picture_spatial_scalable-

| _extension() | macroblock_type tables |  | sequence_scalable_extension() not present |  |  | B-2, B-3 and B-4 |  | 00 | data partitioning |  | B-2, B-3 and B-4 |  | 01 | spatial scalability | present | B-5, B-6 and B-7 |  |  |  | not present | B-2, B-3 and B-4 |  | 10 | SNR scalability |  | B-8 |  | 11 | temporal scalability |  | B-2, B-3 and B-4 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

layer_id - This is an integer which identifies the layers in a scalable hierarchy.  The base layer always has layer_id = 0. However the base layer of a scalable hierarchy does not carry a sequence_scalable_extension() and hence layer_id, except in the case of data partitioning. Each successive layer has a layer_id which is one greater than the layer for which it is an enhancement.

In the case of data partitioning layer_id shall be zero for partition zero and layer_id shall be one for partition one.

lower_layer_prediction_horizontal_size -- this a 14-bit integer indicating the horizontal size of the lower layer frame which is used for prediction.  This shall contain the value contained in horizontal_size (horizontal_size_value and horizontal_size_extension) in the lower layer bitstream.

lower_layer_prediction_vertical_size -- this a 14-bit integer indicating the vertical size of the lower layer frame which is used for prediction.  This shall contain the value contained in vertical_size (vertical_size_value and vertical_size_extension) in the lower layer bitstream.

horizontal_subsampling_factor_m Ñ This affects the spatial scalable upsampling process, as defined in 7.7.2. The value zero is forbidden.

horizontal_subsampling_factor_n Ñ This affects the spatial scalable upsampling process, as defined in 7.7.2. The value zero is forbidden.

vertical_subsampling_factor_m -- This affects the spatial scalable upsampling process, as defined in 7.7.2. The value zero is forbidden.

vertical_subsampling_factor_n Ñ This affects the spatial scalable upsampling process, as defined in 7.7.2. The value zero is forbidden.

picture_mux_enable --  If set to 1, picture_mux_order and picture_mux_factor are used for remultiplexing prior to display.

mux_to_progressive_sequence --  This flag when set to "1" indicates that the decoded pictures corresponding to the two layers shall be temporally multiplexed to generate a progressive sequence for display. When the temporal multiplexing is intended to generate an interlaced sequence this flag shall be "0".

picture_mux_order -- It denotes number of enhancement layer pictures prior to the first base layer picture.  It thus assists remultiplexing of pictures prior to display as it contains information for inverting the demultiplexing performed at the encoder.

picture_mux_factor -- It denotes number of enhancement layer pictures between consecutive base layer pictures to allow correct remultiplexing of base and enhancement layers for display. It also assists in remultiplexing of pictures prior to display as it contains information for inverting the temporal demultiplexing  performed at the encoder.  The value of "000" is reserved.

6.3.9	Group of pictures header

group_start_code -- The group_start_code is the bit string 000001B8 in hexadecimal. It identifies the beginning of a group of pictures header.

time_code -- This is a 25-bit field containing the following: drop_frame_flag, time_code_hours, time_code_minutes, marker_bit, time_code_seconds and time_code_pictures as shown in TableÊ6-11. The fields correspond to the fields defined in the IEC standard for "time and control codes for video tape recorders" (see Bibliography, Annex G). The code refers to the first picture after the group of pictures header that has a temporal_reference of zero. The drop_frame_flag can be set to either "0" or "1". It may be set to "1" only if the frame rate is 29,97Hz. If it is "0" then pictures are counted assuming rounding to the nearest integral number of pictures per second, for example 29,97Hz would be rounded to and counted as 30Hz. If it is "1" then picture numbers 0 and 1 at the start of each minute, except minutes 0, 10, 20, 30, 40, 50 are omitted from the count.

Note	The information carried by time_code plays no part in the decoding process.

TableÊ6-11 --- time_code

| time_code | range of value | No. of bits | Mnemonic |  | drop_frame_flag |  | 1 |  |  | time_code_hours | 0 - 23 | 5 | uimsbf |  | time_code_minutes | 0 - 59 | 6 | uimsbf |  | marker_bit | 1 | 1 | "1" |  | time_code_seconds | 0 - 59 | 6 | uimsbf |  | time_code_pictures | 0 - 59 | 6 | uimsbf |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

closed_gop -- This is a one-bit flag which indicates the nature of the predictions uses in the B-pictures (if any) immediately following the first coded I-frame following the group of picture header .

closed_gop is set to Ò1Ó to indicate that these B-pictures have been encoded using only backward prediction.

This bit is provided for use during any editing which occurs after encoding. If the previous pictures have been removed by editing, broken_link may be set to "1" so that a decoder may avoid displaying these B-Pictures following the first I-Picture following the group of picture header. However if the closed_gop bit is set  to Ò1Õ, then the editor may choose not to set the broken_link bit as these B-Pictures can be correctly decoded.

broken_link -- This is a one-bit flag which shall be set to "0" during encoding. It is set to "1" to indicate that the first B-Pictures (if any) immediately following the first coded I-frame following the group of picture header may not be correctly decoded because the reference frame which is used for prediction is not available (because of the action of editing).

A decoder may use this flag to avoid displaying frames that cannot be correctly decoded.

6.3.10	Picture header

picture_start_code -- The picture_start_code is a string of 32 bits having the value 00000100 in hexadecimal.

temporal_reference -- The temporal_reference is a 10-bit unsigned integer associated with each input picture. It is incremented by one, modulo 1024, for each input frame.  When a frame is coded as two fields the temporal reference in the picture header of both fields is the same.

Following a group start header the temporal reference of the earliest picture (in display order) shall be reset to zero.

picture_coding_type -- The picture_coding_type identifies whether a picture is an intra-coded picture(I), predictive-coded picture(P) or bidirectionally predictive-coded picture(B).  The meaning of picture_coding_type is defined in TableÊ6-12.

Note	Intra-coded pictures with only DC coefficients (D-pictures) that may be used in ISO/IECÊ11172-2 are not supported by this specification.

TableÊ6-12 --- picture_coding_type

| picture_coding_type | coding method |  | 000 | forbidden |  | 001 | intra-coded (I) |  | 010 | predictive-coded (P) |  | 011 | bidirectionally-predictive-coded (B) |  | 100 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

shall not be used

| (dc intra-coded (D) in ISO/IEC11172-2) |  | 101 | reserved |  | 110 | reserved |  | 111 | reserved |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

vbv_delay -- The vbv_delay is a 16-bit unsigned integer. For constant bitrate operation, the vbv_delay is used to set the initial occupancy of the decoder's buffer at the start of play so that the decoder's buffer does not overflow or underflow. The vbv_delay measures the time needed to fill the VBV buffer from an initially empty state at the bitrate, R, to the correct level immediately before the current picture is removed from the buffer.

The value of vbv_delay is the number of periods of the 90kHz system clock that the VBV shall wait after receiving the final byte of the picture start code. It may be calculated from the state of the VBV as follows:

vbv_delayn = 90Ê000 * Bn* / R

where:

n > 0

Bn* =	VBV occupancy, measured in bits, immediately before removing picture n from the buffer but after removing any group of picture header data, sequence header data and the picture_start_code that immediately precedes the data elements of picture n.

R =	the actual bitrate (i.e. to full accuracy rather than the quantised value given by bit_rate in the sequence header.)

For non-constant bitrate operation vbv_delay shall have the value FFFF in hexadecimal. The bitstream shall be either a constant bitrate stream or a variable bitrate stream throughout the sequence.

full_pel_forward_vector -- This flag that is used in ISO/IECÊ11172-2 is not used by this specification.  It shall have the value zero.

forward_f_code -- This parameter that is used in ISO/IECÊ11172-2 is not used by this specification.  It shall have the value seven (all ones).

full_pel_backward_vector -- This flag that is used in ISO/IECÊ11172-2 is not used by this specification.  It shall have the value zero.

backward_f_code -- This parameter that is used in ISO/IECÊ11172-2 is not used by this specification.  It shall have the value seven (all ones).

extra_bit_picture -- A bit indicates the presence of the following extra information. If extra_bit_picture is set to "1", extra_information_picture will follow it. If it is set to "0", there are no data following it. extra_bit_picture shall be set to Ò0Ó, the value Ò1Ó is reserved for possible future extensions defined by ITU-T|ISO/IEC.

extra_information_picture -- Reserved.  A decoder conforming to this specification that encounters extra_information_picture in a bitstream shall ignore it (i.e. parse from bitstream and discard). A bitstream conforming to this specification shall not contain this syntax element.

6.3.11	Picture coding extension

f_code[s][t] -- An unsigned integer taking values 1 through 9 (or 15 if unused). The value zero is forbidden.  In an I-picture in which concealment_motion_vectors is zero (in which case the value of f_code[s][t] is not used in the decoding process) f_code[s][t] shall take the value 15 (all ones).  Similarly, in an I-picture or a P-picture f_code[1][t] is not used in the decoding process (since it refers to backwards motion vectors) and shall take the value 15 (all ones).  (See Table 7-7 for the meaning of the indices; s and t.)

intra_dc_precision - This is a 2-bit integer defined in the TableÊ6-13.

TableÊ6-13 Intra DC precision

| intra_dc_precision | Precision (bits) |  | 00 | 8 |  | 01 | 9 |  | 10 | 10 |  | 11 | 11 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

The inverse quantisation process for the Intra DC coefficients is modified by this parameter as explained in 7.4.1.

picture_structure - This is a 2-bit integer defined in the TableÊ6-14.

TableÊ6-14 Meaning of picture_structure

| picture_structure | Meaning |  | 00 | reserved |  | 01 | Top Field |  | 10 | Bottom Field |  | 11 | Frame picture |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

When a frame is encoded in the form of two field pictures both fields  must be of the same picture_coding_type, except where the first encoded field is an I-picture in which case the second may be either an I-picture or a P-picture.

The first encoded field of a frame may be a top-field or a bottom field, and the next field must be of opposite parity.

When a frame is encoded in the form of two field pictures the following syntax elements may be set independently in each field picture:

¥	f_code[0][0], f_code[0][1]

¥	f_code[1][0], f_code[1][1]

¥	intra_dc_precision, concealment_motion_vectors, q_scale_type

¥	intra_vlc_format, alternate_scan

top_field_first Ñ The meaning of this element depends upon picture_structure, progressive_sequence and repeat_first_field.

If progressive_sequence is equal to 0, this flag indicates what field of a reconstructed frame is output first by the decoding process:

In a field picture top_field_first shall have the value Ò0Ó, and the only field output by the decoding process is the decoded field picture.

In a frame picture top_field_first being set to Ò1Ó indicates that the top field of the reconstructed frame is the first field output by the decoding process.  top_field_first being set to Ò0Ó indicates that the bottom field of the reconstructed frame is the first field output by decoding process

If progressive_sequence is equal to 1, this flag, combined with repeat_first_field, indicates how many times (one, two or three) the  reconstructed frame is output by the decoding process:

If repeat_first_field is set to 0,  top_field_first shall be set to 0.  In this case the output of the decoding process corresponding to this reconstructed frame consists of one progressive frame.

If top_field_first is set to 0 and repeat_first_field is set to 1, the output of the decoding process corresponding to this reconstructed frame consists of two progressive frames.

If top_field_first is set to 1 and repeat_first_field is set to 1, the output of the decoding process corresponding to this reconstructed frame consists of three progressive frames.

frame_pred_frame_dct - If this flag is set to Ò1Ó then only frame-DCT and frame prediction are used. In a field picture it shall be Ò0Ó.  frame_pred_frame_dct shall be Ò1Ó if progressive_frame is Ò1Ó. This flag affects the syntax of the bitstream.

concealment_motion_vectors - This flag has the value Ò1Ó to indicate that motion vectors are coded for intra macroblocks.

q_scale_type - This flag affects the inverse quantisation process as described in 7.4.2.2.

intra_vlc_format -- This flag affects the decoding of transform coefficient data as described in 7.2.2.1.

alternate_scan -- This flag affects the decoding of transform coefficient data as described in 7.3.

repeat_first_field -- This flag is applicable only in a frame picture, in a field picture it shall be set to zero and does not affect the decoding process.

If progressive_sequence is equal to 0 and progressive_frame is equal to 0, repeat_first_field shall be zero, and the output of the decoding process corresponding to this reconstructed frame consists of two fields.

If progressive_sequence is equal to 0 and progressive_frame is equal to 1:

If this flag is set to 0, the output of the decoding process corresponding to this reconstructed frame consists of two fields.  The first field (top or bottom field as identified by top_field_first) is followed by the other field.

If it is set to 1, the output of the decoding process corresponding to this reconstructed frame consists of three fields.  The first field (top or bottom field as identified by top_field_first) is followed by the other field, then the first field is repeated.

If progressive_sequence is equal to 1:

If this flag is set to 0, the output of the decoding process corresponding to this reconstructed frame consists of one frame.

If it is set to 1, the output of the decoding process corresponding to this reconstructed  frame consists of two or three frames, depending on the value of top_field_first.

chroma_420_type -  If chroma_format is "4:2:0",  the value of chroma_420_type shall be the same as progressive_frame; else chroma_420_type has no meaning and shall be equal to zero.  This flag exists for historical reasons.

progressive_frame Ñ If progressive_frame is set to 0 it indicates that the two fields of the frame are interlaced fields in which an interval of time of the field period exists between (corresponding spatial samples) of the two fields.  In this case the following restriction applies:

¥	repeat_first_field shall be zero (two field duration).

If progressive_frame is set to 1 it indicates that the two fields (of the frame) are actually from the same time instant as one another.  In this case a number of restrictions to other parameters and flags in the bitstream apply:

¥	picture_structure shall be ÒFrameÓ

¥	frame_pred_frame_dct shall be 1

This parameter is used when the video sequence is used as the lower layer of a spatial scalable sequence.  Here it affects the up-sampling process used in forming a prediction in the enhancement layer from the lower layer.

composite_display_flag Ñ This flag is set to 1 to indicate that the following fields that are of use when the input pictures have been coded as (analogue) composite video prior to encoding into a bitstream that complies with this specification.  If it is set to 0 then these parameters do not occur in the bitstream.

The information relates to the picture that immediately follows the extension.  In the case that this picture is a frame picture the information relates to the first field of that frame.  The equivalent information for the second field may be derived (there is no way to represent it in the bitstream).

Note that repeat_first_field will cause a composite video field to be repeated out of colour field sequence.  It is recommended that repeat_first_field and composite_display_flag are not both set simultaneously.

v_axis -- A 1-bit integer used only when the bitstream represents a signal that had previously been encoded according to PAL systems. v_axis is set to 1 on a positive sign, v_axis is set to 0 otherwise.

field_sequence -- A 3-bit integer which defines the number of the field in the eight field sequence used in PAL systems or the four field sequence used in NTSC systems as defined in the TableÊ6-15.

TableÊ6-15 Definition of field_sequence.

| field sequence | frame | field |  | 000 | 1 | 1 |  | 001 | 1 | 2 |  | 010 | 2 | 3 |  | 011 | 2 | 4 |  | 100 | 3 | 5 |  | 101 | 3 | 6 |  | 110 | 4 | 7 |  | 111 | 4 | 8 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

sub_carrier -- This is a 1-bit integer. Set to 0 means the sub-carrier/line frequency relationship is correct.  When set to 1 the relationship is not correct.

burst_amplitude -- This is a 7-bit integer defining the burst amplitude (for PAL and NTSC only). The amplitude of the sub-carrier burst is quantised as a ITU-R Recommendation 601 luminance signal, with the MSB omitted.

sub_carrier_phase -- This is an 8-bit integer defining the phase of the  reference sub-carrier at the field-synchronisation datum with respect, to field start as defined in ITU-R Recommendation 470. See TableÊ6-16.

TableÊ6-16 Definition of sub_carrier_phase.

| sub_carrier_phase | Phase |  | 0 | ([360oÖ256] * 0) |  | 1 | ([360oÖ256] * 1) |  | ... | ... |  | 255 | ([360oÖ256] * 255) |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.3.7	Quant matrix extension

Each quantisation matrix has a default set of values.  When a sequence_header_code is decoded all matrices shall be reset to their default values.  User defined matrices may be downloaded and this can occur in a sequence_header() or in a quant_matrix_extension().

With 4:2:0 data only two matrices are used, one for intra blocks the other for non-intra blocks.

With 4:2:2 or 4:4:4 data four matrices are used.  Both an intra and a non-intra matrix are provided for both luminance blocks and for chrominance blocks.  Note however that it is possible to download the same user defined matrix into both the luminance and chrominance matrix at the same time.

The default matrix for intra blocks (both luminance and chrominance) is:

| 8 | 16 | 19 | 22 | 26 | 27 | 29 | 34 |  | 16 | 16 | 22 | 24 | 27 | 29 | 34 | 37 |  | 19 | 22 | 26 | 27 | 29 | 34 | 34 | 38 |  | 22 | 22 | 26 | 27 | 29 | 34 | 37 | 40 |  | 22 | 26 | 27 | 29 | 32 | 35 | 40 | 48 |  | 26 | 27 | 29 | 32 | 35 | 40 | 48 | 58 |  | 26 | 27 | 29 | 34 | 38 | 46 | 56 | 69 |  | 27 | 29 | 35 | 38 | 46 | 56 | 69 | 83 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

The default matrix for non-intra blocks (both luminance and chrominance) is:

| 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

load_intra_quantiser_matrix -- This is a one-bit flag which is set to "1" if intra_quantiser_matrix follows.  If it is set to "0" then there is no change in the values that shall be used.  Note that if this flag is zero in a sequence_header() the default values will be used because the sequence_header_code will reset the matrices to their defaults.

intra_quantiser_matrix -- This is a list of sixty-four 8-bit unsigned integers. The new values, encoded in the default zigzag scanning order as described in 7.3.1, replace the previous values. The first value shall always be 8. For all of the 8-bit unsigned integers, the value zero is forbidden.  With 4:2:2 and 4:4:4 data the new values shall be used for both the luminance intra matrix and the chrominance intra matrix.  However the chrominance intra matrix may subsequently be loaded with a different matrix.

load_non_intra_quantiser_matrix -- This is a one-bit flag which is set to "1" if non_intra_quantiser_matrix follows.  If it is set to "0" then there is no change in the values that shall be used.  Note that if this flag is zero in a sequence_header() the default values will be used because the sequence_header_code will reset the matrices to their defaults.

non_intra_quantiser_matrix -- This is a list of sixty-four 8-bit unsigned integers. The new values, encoded in the default zigzag scanning order as described in 7.3.1, replace the previous values. For the 8-bit unsigned integers, the value zero is forbidden.  With 4:2:2 and 4:4:4 data the new values shall be used for both the luminance non-intra matrix and the chrominance non-intra matrix.  However the chrominance non-intra matrix may subsequently be loaded with a different matrix.

load_chroma_intra_quantiser_matrix -- This is a one-bit flag which is set to "1" if chroma_intra_quantiser_matrix follows.  If it is set to "0" then there is no change in the values that shall be used.  If chroma_format is Ò4:2:0Ó this flag shall take the value Ò0Ó.

chroma_intra_quantiser_matrix -- This is a list of sixty-four 8-bit unsigned integers. The new values, encoded in the default zigzag scanning order as described in 7.3.1, replace the previous values. The first value shall always be 8. For all of the 8-bit unsigned integers, the value zero is forbidden.

load_chroma_non_intra_quantiser_matrix -- This is a one-bit flag which is set to "1" if chroma_non_intra_quantiser_matrix follows.  If it is set to "0" then there is no change in the values that shall be used.  If chroma_format is Ò4:2:0Ó this flag shall take the value Ò0Ó.

chroma_non_intra_quantiser_matrix -- This is a list of sixty-four 8-bit unsigned integers. The new values, encoded in the default zigzag scanning order as described in 7.3.1, replace the previous values. For the 8-bit unsigned integers, the value zero is forbidden.

6.3.12	Picture display extension

This specification does not define the display process. The information in this extension does not affect the decoding process and may be ignored by decoders that conform to this specification.

The picture display extension allows the position of the display rectangle whose size is specified in sequence_display_extension() to be moved on a picture-by-picture basis.  One application for this is the implementation of pan-scan.

frame_centre_horizontal_offset Ñ This is a 16-bit signed integer giving the horizontal offset in units of 1/16th sample.  A positive value shall indicate that the centre of the reconstructed frame lies to the right of the centre of the display rectangle.

frame_centre_vertical_offset Ñ This is a 16-bit signed integer giving the vertical offset in units of 1/16th sample.  A positive value shall indicate that the centre of the reconstructed frame lies below the centre of the display rectangle.

The dimensions of the rectangular region are defined in the sequence_display_extension().  The coordinates of the region within the coded picture are defined in the picture_display_extension().  Since (in the case of an interlaced sequence) a coded picture may relate to one, two or three decoded fields the picture_display_extension() may contain up to three offsets.

The number of frame centre offsets in the picture_display_extension() shall be defined as follows:

if (( progressive_sequence == 1) || (picture_structure == ÒfieldÓ)) {

number_of_frame_centre_offsets = 1

} else {

if (repeat_first_field == Ò1Ó )

number_of_frame_centre_offsets = 3

else

number_of_frame_centre_offsets = 2

}

A picture_display_extension() shall not occur unless a sequence_display_extension() followed the previous sequence_header().

In the case that a given picture does not have a picture_display_extension() then the most recently decoded frame centre offset shall be used.  Note that each of the missing frame centre offsets have the same value (even if two or three frame centre offstes would have been contained in the picture_display_extension() had been present).  Following a sequence_header() the value zero shall be used for all frame centre offsets until a picture_display_extension() defines non-zero values.

Figure 6-18 illustrates the picture display parameters.  As shown the frame centre offsets contained in the picture_display_extension() shall specify the position of the centre of the reconstructed frame from the centre of the display rectangle.

Note	The display rectangle may also be larger than the reconstructed frame.

Figure 6-18.  Frame  centre offset parameters

Note	Even in a field picture the frame_centre_vertical_offset still represents the offset of the centre of the frame in 1/16ths of a frame line (not a line in the field).

6.3.12.1	Pan-scan

The frame centre offsets may be used to implement pan-scan in which a rectangular region is defined which may be panned around the entire reconstructed frame.

By way of example only; this facility may be used to identify a 3/4 aspect ratio window in a 9/16 coded picture format.  This would allow a decoder to produce usable pictures for a conventional definition television set from an encoded format intended for enhanced definition.  The 3/4 aspect ratio region is intended to contain the Òmost interestingÓ region of the picture.

The 3/4 region is defined by display_horizontal_size and display_vertical_size.  The 9/16 frame size is defined by horizontal_size and vertical_size.

6.3.14	Picture temporal scalable extension

reference_select_code -- This is a 2-bit code that identifies reference frames or reference fields for prediction  depending on the picture type.

forward_temporal_reference -- An unsigned integer value which indicates temporal reference of the lower layer frame to be used to provide the forward prediction. If the lower layer indicates temporal reference with more than 10 bits, the least significant bits are encoded here. If the lower layer indicates temporal reference with fewer than 10 bits, all bits are encoded here and the more significant bits shall be set to zero.

backward_temporal_reference -- An unsigned integer value which indicates temporal reference of the lower layer frame to be used to provide the backward prediction. If the lower layer indicates temporal reference with more than 10 bits, the least significant bits are encoded here. If the lower layer indicates temporal reference with fewer than 10 bits, all bits are encoded here and the more significant bits shall be set to zero.

6.3.13	Picture spatial scalable extension

lower_layer_temporal_reference - An unsigned integer value which indicates temporal reference of the lower layer frame to be used to provide the prediction. If the lower layer indicates temporal reference with more than 10 bits, the least significant bits are encoded here. If the lower layer indicates temporal reference with fewer than 10 bits, all bits are encoded here and the more significant bits shall be set to zero.

lower_layer_horizontal_offset - This signed integer specifies the horizontal offset of the (top left hand corner) of the upsampled lower layer frame relative to the enhancement layer picture.  It is expressed in units of the enhancement layer picture sample width.  If the chrominance format is 4:2:0 or 4:2:2 then this parameter shall be an even number.

lower_layer_vertical_offset -  This signed integer specifies the vertical offset of the (top left hand corner) of the upsampled lower layer picture relative to the enhancement layer picture.  It is expressed in units of the enhancement layer picture sample height.  If the chrominance format is 4:2:0 then this parameter shall be an even number.

spatial_temporal_weight_code_table_index -- This indicates which TableÊof spatial temporal weight codes is to be used as defined in 7.7. Permissible values of spatial_temporal_weight_code_table_index are defined in Table 7-20.

lower_layer_progressive_frame -- This flag shall be set to 0 if the lower layer frame is nterlaced and shall be set to "1" if the lower layer frame is progressive. The use of this flag in the spatial scalable upsampling process is defined in 7.7.

lower_layer_deinterlaced_field_select -- This affects the spatial scalable upsampling process, as defined in 7.7.

6.3.15	Slice

slice_start_code -- The slice_start_code is a string of 32-bits. The first 24-bits have the value 000001 in hexadecimal and the last 8-bits are the slice_vertical_position having a value in the range 01 through AF hexadecimal inclusive.

slice_vertical_position -- This is given by the last eight bits of the slice_start_code. It is an unsigned integer giving the vertical position in macroblock units of the first macroblock in the slice.

In large pictures (when the vertical size of the frame is greater than 2800 lines) the slice vertical position is extended by the slice_vertical_position_extension.

The macroblock row may be calculated as follows:

if ( vertical_size > 2800 )

mb_row = (slice_vertical_position_extension << 7) + slice_vertical_position - 1;

else

mb_row = slice_vertical_position - 1;

The slice_vertical_position of the first row of macroblocks is one. Some slices may have the same slice_vertical_position, since slices may start and finish anywhere. The maximum value of slice_vertical_position is 175 unless slice_vertical_position_extension is present in which case slice_vertical_position shall be in the range [1:128].

priority_breakpoint Ñ This is a 7-bit integer that indicates the point in the syntax where the bitstream shall be partitioned. The allowed values and their semantic interpretation is given in TableÊ7-28.  priority_breakpoint shall take the value zero in partition 1.

quantiser_scale_code -- An unsigned integer in the range 1 to 31 . The decoder shall use this value until another quantiser_scale_code is encountered either in slice() or macroblock(). The value zero is forbidden.

intra_slice_flag - This flag shall be set to Ò1Ó to indicate the presence of intra_slice and reserved_bits in the bitstream.

intra_slice - This shall be set to Ò0Ó if any of the macroblocks in the slice are non-intra macroblocks.  If all of the macroblocks are intra macroblocks then intra_slice may be set to Ò1Ó.  intra_slice may be omitted from the bitstream (by setting intra_slice_flag to Ò0Ó) in which case it shall be assumed to have the value zero.

intra_slice is not used by the decoding process.  intra_slice is intended to aid a DSM application in performing FF/FR (see D.11).

reserved_bits - These seven bits shall have the value zero.

extra_bit_slice -- A bit indicates the presence of the following extra information. If extra_bit_slice is set to "1", extra_information_slice will follow it. If it is set to "0", there are no data following it. extra_bit_slice shall be set to Ò0Ó, the value Ò1Ó is reserved for possible future extensions defined by ITU-T|ISO/IEC.

extra_information_slice -- Reserved.  A decoder conforming to this specification that encounters extra_information_slice in a bitstream shall ignore it (i.e. parse from bitstream and discard). A bitstream conforming to this specification shall not contain this syntax element.

6.3.16	Macroblock

Note	Òmacroblock_stuffingÓ which is supported in ISO/IEC11172-2 shall not be used in a bitstream defined by this specification.

macroblock_escape -- The macroblock_escape is a fixed bit-string "0000 0001 000" which is used when the difference between macroblock_address and previous_macroblock_address is greater than 33. It causes the value of macroblock_address_increment to be 33 greater than the value that will be decoded by subsequent macroblock_escapes and the macroblock_address_increment codewords.

For example, if there are two macroblock_escape codewords preceding the macroblock_address_increment, then 66 is added to the value indicated by macroblock_address_increment.

macroblock_address_increment Ñ This is a variable length coded integer coded as per Annex B TableÊB-1 which indicates the difference between macroblock_address and previous_macroblock_address. The maximum value of macroblock_address_increment is 33. Values greater than this can be encoded using the macroblock_escape codeword.

The macroblock_address is a variable defining the absolute position of the current macroblock. The macroblock_address of the top-left macroblock is zero.

The previous_macroblock_address is a variable defining the absolute position of the last non-skipped macroblock (see 7.6.6 for the definition of skipped macroblocks) except at the start of a slice. At the start of a slice previous_macroblock_address is reset as follows:

previous_macroblock_address = (mb_row * mb_width) -1

The horizontal spatial position in macroblock units of a macroblock in the picture (mb_column) can be computed from the macroblock_address as follows:

mb_column = macroblock_address % mb_width

where mb_width is the number of macroblocks in one row of the picture.

Except at the start of a slice, if the value of macroblock_address recovered from macroblock_address_increment and the macroblock_escape codes (if any) differs from the previous_macroblock_address by more than one then some macroblocks have been skipped.  It is a requirement that;

¥	There shall be no skipped macroblocks in I-pictures except when

either	picture_spatial_scalable_extension() follows the picture_header() of the current picture.

or	sequence_scalable_extension() is present in the bitstream and scalable_mode = ÒSNR scalabilityÓ.

¥	The first and last macroblock of a slice shall not be skipped.

¥	In a B-picture there shall be no skipped macroblocks immediately following a macroblock in which macroblock_intra is one.

6.3.16.1	Macroblock modes

macroblock_type -- Variable length coded indicator which indicates the method of coding and content of the macroblock according to the Tables B-2 through B-8, selected by picture_coding_type and scalable_mode.

macroblock_quant -- Derived from macroblock_type according to the Tables B-2 through B-8. This is set to 1 to indicate that quant_scale_code is present in the bitstream.

macroblock_motion_forward -- Derived from macroblock_type according to the Tables B-2 through B-8. This flag affects the bitstream syntax and is used by the decoding process.

macroblock_motion_backward -- Derived from macroblock_type according to the Tables B-2 through B-8. This flag affects the bitstream syntax and is used by the decoding process.

macroblock_pattern -- Derived from macroblock_type according to the Tables B-2 through B-8. This is set to 1 to indicate that coded_block_pattern() is present in the bitstream.

macroblock_intra -- Derived from macroblock_type according to the Tables B-2 through B-8. This flag affects the bitstream syntax and is used by the decoding process.

spatial_temporal_weight_code_flag -- Derived from the macroblock_type. This indicates whether the spatial_temporal_weight_code is present in the bitstream.

spatial_temporal_weight_code -- This is a two bit code which indicates, in the case of spatial scalability, how the spatial and temporal predictions shall be combined to form the prediction for the macroblock.  A full description of how to form the spatial scalable prediction is given in 7.7.

frame_motion_type - This is a two bit code indicating the macroblock motion prediction, defined in TableÊ6-17.

If frame_pred_frame_dct is equal to 1 then frame_motion_type is omitted from the bitstream.  In this case motion vector decoding and prediction formation shall be performed as if frame_motion_type had indicated ÒFrame-based predictionÓ.

In the case of intra macroblocks (in a frame picture) when concealment_motion_vectors is equal to 1 frame_motion_type is not present in the bitstream. In this case motion vector decoding and update of the motion vector predictors shall be performed as if frame_motion_type had indicated ÒFrame-based predictionÓ.  See 7.6.3.9.

TableÊ6-17 Meaning of frame_motion_type

code

spatial_temporal

| _weight_class | prediction type |
| --- | --- |

motion_vector

| _count | mv_format | dmv |  | 00 |  | reserved |  |  |  |  | 01 | 0,1 | Field-based prediction | 2 | field | 0 |  | 01 | 2,3 | Field-based prediction | 1 | field | 0 |  | 10 | 0,1,2,3 | Frame-based prediction | 1 | frame | 0 |  | 11 | 0,2,3 | Dual-Prime | 1 | field | 1 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

field_motion_type - This is a two bit code indicating the macroblock motion prediction, defined in TableÊ6-18.

In the case of intra macroblocks (in a field picture) when concealment_motion_vectors is equal to 1 field_motion_type is not present in the bitstream. In this case motion vector decoding and update of the motion vector predictors shall be performed shall be performed as if field_motion_type had indicated ÒField-based predictionÓ.  See 7.6.3.9.

TableÊ6-18 Meaning of field_motion_type

code

spatial_temporal

| _weight_class | prediction type |
| --- | --- |

motion_vector

| _count | mv_format | dmv |  | 00 |  | reserved |  |  |  |  | 01 | 0,1 | Field-based prediction | 1 | field | 0 |  | 10 | 0,1 | 16x8 MC | 2 | field | 0 |  | 11 | 0 | Dual-Prime | 1 | field | 1 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

decode_dct_type - This is a flag (derived from various bitstream elements) that determines whether the following syntax element dct_type is present in the bitstream. It is derived as follows:

if ( (picture_structure == ÒframeÓ ) && (frame_pred_frame_dct == 0) &&

(macroblock_intra || macroblock_pattern) ) {

decode_dct_type = 1;

} else

decode_dct_type = 0;

dct_type - This is a flag indicating whether the macroblock is frame DCT coded or field DCT coded. If this is set to "1", the macroblock is field DCT coded.  dct_type is only included in the bitstream if decode_dct_type is non-zero.

In the case that decode_dct_type is zero then dct_type (used in the remainder of the decoding process) shall be derived as shown in TableÊ6-19.

TableÊ6-19. Value of dct_type if dct_type is not in the bitstream.

| Condition | dct_type |  | picture_structure == ÒfieldÓ | unused because there is no frame/field distinction in a field picture. |  | frame_pred_frame_dct == 1 | 0 (ÒframeÓ) |  | !(macroblock_intra ¦¦ macroblock_pattern) | unused - macroblock is not coded |  | macroblock is skipped | unused - macroblock is not coded |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.3.16.2	Motion vectors

motion_vector_count is derived from field_motion_type or frame_motion_type as indicated in TableÊ6-17 and TableÊ6-18.

mv_format is derived from field_motion_type or frame_motion_type as indicated in the TableÊ6-17 and TableÊ6-18. mv_format indicates if the motion vector is a field-motion vector or a frame-motion vector. mv_format is used in the syntax of the motion vectors and in the process of motion vector prediction.

dmv is derived from field_motion_type or frame_motion_type as indicated in TableÊ6-17 and TableÊ6-18

motion_vertical_field_select[r][s] Ñ This flag indicates which reference field shall be used to form the prediction.  If motion_vertical_field_select[r][s] is zero then the top reference field shall be used, if it is one then the bottom reference field shall be used.  (See Table 7-7 for the meaning of the indices; r and s.)

6.3.16.3	Motion vector

motion_code[r][s][t] Ñ This is a variable length code which is used in motion vector decoding as described in 7.6.3.1.  (See Table 7-7 for the meaning of the indices; r, s and t.)

motion_residual[r][s][t] Ñ This is an integer which is used in motion vector decoding as described in 7.6.3.1.    (See Table 7-7 for the meaning of the indices; r, s and t.)  The number of bits in the bitstream for motion_residual[r][s][t], r_size, is derived from f_code[s][t] as follows;

r_size = f_code[s][t] - 1

Note:	The number of bits for both motion_residual[0][s][t] and motion_residual[1][s][t] is denoted by f_code[s][t].

dmvector[t] Ñ This is a variable length code which is used in motion vector decoding as described in 7.6.3.1.  (See Table 7-7 for the meaning of the index; t.)

6.3.16.3	Coded block patern

coded_block_pattern_420 Ñ A variable length code that is used to derive the variable cbp according to TableÊB-9.

coded_block_pattern_1 Ñ

coded_block_pattern_2 Ñ For 4:2:2 and 4:4:4 data the coded block pattern is extended by the addition of either a two bit or six bit fixed length code, coded_block_pattern_1 or coded_block_pattern_2. Then the pattern_code[i] is derived from cbp using the following:

for (i=0; i<12; i++)

if (macroblock_intra != 0)

pattern_code[i] = 1;

else

pattern_code[i] = 0;

if (macroblock_intra == 0) {

for (i=0; i<6; i++)

if ( cbp & (1<<(5-i)) ) pattern_code[i] = 1;

if (chroma_format == Ò4:2:2Ó)

for (i=6; i<8; i++)

if ( coded_block_pattern_1 & (1<<(7-i)) ) pattern_code[i] = 1;

if (chroma_format == Ò4:4:4Ó)

for (i=6; i<12; i++)

if ( coded_block_pattern_2 & (1<<(11-i)) ) pattern_code[i] = 1;

}

If pattern_code[i] equals to 1, i=0 to (block_count-1), then the block number i defined in Figures 6-8, 6-9 and 6-10 is contained in this macroblock.

The number Òblock_countÓ which determines the number of blocks in the macroblock is derived from the chrominance format as shown in TableÊ6-20.

TableÊ6-20 block_count as a function of chroma_format

| chroma_format | block_count |  | 4:2:0 | 6 |  | 4:2:2 | 8 |  | 4:4:4 | 12 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

6.3.17	Block

The semantics of block() are described in clauseÊ 7.

7	The video decoding process

This clause specifies the decoding process that a decoder shall perform to recover picture data from the coded bitstream.

With the exception of the Inverse Discrete Cosine Transform (IDCT) the decoding process is defined such that all decoders shall produce numerically identical results.  Any decoding process that produces identical results to the process described here, by definition, complies with this specification.

The IDCT is defined statistically in order that different implementations for this function are allowed.  The IDCT specification is given in Annex A.

In 7.1 through 7.6 the simplest decoding process is specified in which no scalability features are used. 7.7 to 7.11 specify the decoding process when scalable extensions are used.

Figure 7-1 is a diagram of the Video Decoding Process without any scaling.  The diagram is simplified for clarity.

Note	Throughout this specification two dimensional arrays are represented as name[q][p] where ÔqÕ is the index in the vertical dimension and ÔpÕ the index in the horizontal dimension.

Figure 7-1.  Simplified Video Decoding Process

7.1	Higher syntactic structures

The various parameters and flags in the bitstream for macroblock() and all syntactic structures above macroblock() shall be interpreted as indicated in clauseÊ 6.  Many of these parameters and flags affect the decoding process described in the following clauses.  Once all of the macroblocks in a given picture have been processed the entire picture will have been reconstructed.

Reconstructed field pictures shall be associated together in pairs to form reconstructed frames. (See Òpicture_structureÓ in 6.3.11.)

The sequence of reconstructed frames shall be reordered as described in 6.1.1.1.

If progressive_sequenceÊ==Ê1 the reconstructed frames shall be output from the decoding process at regular intervals of the frame period as shown in Figure 6-15.

If progressive_sequenceÊ==Ê0 the reconstructed frames shall be broken into a sequence of fields which shall be output from the decoding process at regular intervals of the field period as shown in Figure 6-16.  In the case that a frame picture has repeat_first_fieldÊ==Ê1 the first field of the frame shall be repeated after the second field. (See Òrepeat_first_fieldÓ in 6.3.11.)

7.2	Variable length decoding

7.2.1 specifies the decoding process used for the DC coefficient (n=0) in an intra coded block. (n is the index of the coefficient in the appropriate zig-zag scan order.)  7.2.2 specifies the decoding process for all other coefficients; AC coefficients (n­0) and DC coefficients in non-intra coded blocks.

Let cc denote the colour component.  It is related to the block number as specified in TableÊ7-1.  Thus cc is zero for the Y component, one for the Cb component and two for the Cr component.

TableÊ7-1. Definition of cc, colour component index

|  | cc |  |  |  | Block Number | 4:2:0 | 4:2:2 | 4:4:4 |  | 0 | 0 | 0 | 0 |  | 1 | 0 | 0 | 0 |  | 2 | 0 | 0 | 0 |  | 3 | 0 | 0 | 0 |  | 4 | 1 | 1 | 1 |  | 5 | 2 | 2 | 2 |  | 6 |  | 1 | 1 |  | 7 |  | 2 | 2 |  | 8 |  |  | 1 |  | 9 |  |  | 2 |  | 10 |  |  | 1 |  | 11 |  |  | 2 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

7.2.1	DC coefficients in intra blocks

DC coefficients in blocks in intra macroblocks are encoded as a variable length code denoting dct_dc_size as defined in TableÊB-12 and B-13.  If dct_dc_size is not equal to zero then this shall be followed by a fixed length code, dc_dct_differential, of dct_dc_size bits.  A differential value is first recovered from the coded data which is added to a predictor in order to recover the final decoded coefficient.

If cc is zero then TableÊB-12 shall be used for dct_dc_size.  If cc is non-zero then TableÊB-13 shall be used for dct_dc_size.

Three predictors are maintained, one for each of the colour components, cc. Each time a DC coefficient in a block in an intra macroblock is decoded the predictor is added to the differential to recover the actual coefficient. Then the predictor shall be set to the value of the coefficient just decoded.  At various times, as described below, the predictors shall be reset.  The reset value is derived from the parameter intra_dc_precision as specified in TableÊ7-2.

TableÊ7-2. Relation between intra_dc_precision and the predictor reset value

| intra_dc_precision | Bits of precision | reset value |  | 0 | 8 | 128 |  | 1 | 9 | 256 |  | 2 | 10 | 512 |  | 3 | 11 | 1024 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

The predictors shall be reset to the reset value at the following times:

¥	At the start of a slice.

¥	Whenever a non-intra macroblock is decoded.

¥	Whenever a macroblock is skipped. i.e. when macroblock_address_increment > 1.

The predictors are denoted dc_dct_pred[cc].

QFS[0] shall be calculated from dc_dct_size and dc_dct_differential by any process equivalent to:

if ( dc_dct_size == 0 ) {

dct_diff = 0;

} else {

half_range = 2 ^ ( dc_dct_size - 1 );				Note ^ denotes power (not XOR)

if ( dc_dct_differential >= half_range )

dct_diff = dc_dct_differential;

else

dct_diff = (dc_dct_differential + 1) - (2 * half_range);

}

QFS[0] = dc_dct_pred[cc] + dct_diff;

dc_dct_pred[cc] = QFS[0]

Note	dct_diff and half_range are temporary variables which are not used elsewhere in this specification.

It is a requirement of the bitstream that QFS[0] shall lie in the range;

0 to ((2^(8 + intra_dc_precision))-1)

7.2.2	Other coefficients

All coefficients with the exception of the DC intra coefficients shall be encoded using Tables B-14, B-15 and B-16.

In all cases a variable length code shall first be decoded using either TableÊB-14 or TableÊB-15.  The decoded value of this code denotes one of three courses of action:

1	End of Block.  In this case there are no more coefficients in the block in which case the remainder of the coefficients in the block (those for which no value has yet been decoded) shall be set to zero.  This is denoted by ÒEnd of blockÓ in the syntax specification of 6.2.6.

2	A ÒnormalÓ coefficient in which a value of run and level is decoded followed by a single bit, s, giving the sign of the coefficient  signed_level is computed from level and s as shown below.  run coefficients shall be set to zero and the subsequent coefficient shall have the value signed_level.

if (s ==0)

signed_level = level;

else

signed_level = (-level);

3	An ÒEscapeÓ coded coefficient.  In which the values of run and signed_level are fixed length coded as described in 7.2.2.3.

7.2.2.1	TableÊselection

TableÊ7-3 indicates which TableÊshall be used for decoding the DCT coefficients.

TableÊ7-3. Selection of DCT coefficient VLC tables

| intra_vlc_format | 0 | 1 |  |
| --- | --- | --- | --- |

intra blocks

| (macroblock_intra = 1) | B-14 | B-15 |  |
| --- | --- | --- | --- |

non-intra blocks

| (macroblock_intra = 0) | B-14 | B-14 |  |
| --- | --- | --- | --- |

7.2.2.2	First coefficient of a non-intra block

In the case of the first coefficient of a non-intra block (a block in a non-intra macroblock) TableÊB-14 is modified as indicated by ÒNOTEÊ2Ó and ÒNOTEÊ3Ó at the foot of that Table.

This modification only affects the entry that represents run = 0, level = ±1.   Since it is not possible to encode an EndÊofÊblock as the first coefficient of a block (the block would be Ònot codedÓ in this case) no possibility for ambiguity exists.

The positions in the syntax that use this modified TableÊare denoted by ÒFirst DCT coefficientÓ in the syntax specification of 6.2.6.  The remainder of the coefficients are denoted by ÒSubsequent DCT coefficientsÓ.

Note	In the case that TableÊB-14 is used for an intra block, the first coefficient shall be coded as specified in 7.2.1.  TableÊB-14 shall therefore not be modified as the first coefficient that uses TableÊB-14 is the second coefficient in the block.

7.2.2.3	Escape coding

Many possible combinations of run and level have no variable length code to represent them.  In order to encode these statistically rare combinations an Escape coding method is used.

TableÊB-16 defines the escape coding method.  The Escape VLC is followed by a 6-bit fixed length code giving ÒrunÓ. This is followed by a 12-bit fixed length code giving the values of Òsigned_levelÓ.

Note	Attention is drawn to the fact that the escape coding method used in this specification is different to that used in ISO/IEC 11172-2.

7.2.2.4	Summary

To summarise 7.2.2. The variable length decoding process shall be equivalent to the following.  At the start of this process n shall take the value zero for non-intra blocks and one for intra blocks.

eob_not_read = 1;

while ( eob_not_read )

{

<decode VLC, decode Escape coded coefficient if required>

if ( <decoded VLC indicates EndÊofÊblock> ) {

eob_not_read = 0;

while ( n< 64) {

QFS[n] = 0;

n = n + 1;

}

} else {

for ( m = 0; m < run; m++ ) {

QFS[n] = 0;

n = n + 1;

}

QFS[n] = signed_level

n = n + 1;

}

}

Note	eob_not_read and m are temporary variables that are not used elsewhere in this specification.

7.3	Inverse scan

Let the data at the output of the variable length decoder be denoted by QFS[n].  n is in the range 0 to 63.

This clause specifies the way in which the one-dimensional data, QFS[n], is converted into a two-dimensional array of coefficients denoted by QF[v][u].  u and v both lie in the range 0 to 7.

Two scan patterns are defined.  The scan that shall be used shall be determined by alternate_scan which is encoded in the picture header extension.

Figure 7-1 defines scan[alternate_scan][v][u] for the case that alternate_scan is zero. Figure 7-2 defines scan[alternate_scan][v][u] for the case that alternate_scan is one.

|  |  |  |  |  |  |  |  |  | u |  |  |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  | 0 | 0 | 1 | 5 | 6 | 14 | 15 | 27 | 28 |  |  | 1 | 2 | 4 | 7 | 13 | 16 | 26 | 29 | 42 |  |  | 2 | 3 | 8 | 12 | 17 | 25 | 30 | 41 | 43 |  |  | 3 | 9 | 11 | 18 | 24 | 31 | 40 | 44 | 53 |  |  | 4 | 10 | 19 | 23 | 32 | 39 | 45 | 52 | 54 |  |  | 5 | 20 | 22 | 33 | 38 | 46 | 51 | 55 | 60 |  |  | 6 | 21 | 34 | 37 | 47 | 50 | 56 | 59 | 61 |  | v | 7 | 35 | 36 | 48 | 49 | 57 | 58 | 62 | 63 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Figure 7-1. Definition of scan[0][v][u]

|  |  |  |  |  |  |  |  |  | u |  |  |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  | 0 | 0 | 4 | 6 | 20 | 22 | 36 | 38 | 52 |  |  | 1 | 1 | 5 | 7 | 21 | 23 | 37 | 39 | 53 |  |  | 2 | 2 | 8 | 19 | 24 | 34 | 40 | 50 | 54 |  |  | 3 | 3 | 9 | 18 | 25 | 35 | 41 | 51 | 55 |  |  | 4 | 10 | 17 | 26 | 30 | 42 | 46 | 56 | 60 |  |  | 5 | 11 | 16 | 27 | 31 | 43 | 47 | 57 | 61 |  |  | 6 | 12 | 15 | 28 | 32 | 44 | 48 | 58 | 62 |  | v | 7 | 13 | 14 | 29 | 33 | 45 | 49 | 59 | 63 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Figure 7-2. Definition of scan[1][v][u]

The inverse scan shall be any process equivalent to the following:

for (v=0; v<8; v++)

for (u=0; u<8; u++)

QF[v][u] = QFS[scan[alternate_scan][v][u]]

7.3.1	Inverse scan for matrix download

When the quantisation matrices are downloaded they are encoded in the bitstream in a scan order that is converted into the two-dimensional matrix used in the inverse quantiser in an identical manner to that used for coefficients.

For matrix download the scan defined by Figure 7-1 (i.e. scan zero) shall always be used.

Let W[w][u][v] denote the weighting matrix in the inverse quantiser (see 7.4.2.1), and WÕ[w][n] denote the matrix as it is encoded in the bitstream.  The matrix download shall then be equivalent to the following:

for (v=0; v<8; v++)

for (u=0; u<8; u++)

W[w][v][u] = WÕ[w][scan[0][v][u]]

7.4	Inverse quantisation

The two-dimensional array of coefficients, QF[v][u], is inverse quantised to produce the reconstructed DCT coefficients.  This process is essentially a multiplication by the quantiser step size.  The quantiser step size is modified by two mechanisms; a weighting matrix is used to modify the step size within a block and a scale factor is used in order that the step size can be modified at the cost of only a few bits (as compared to encoding an entire new weighting matrix).

Figure 7-3. Inverse quantisation process

Figure 7-3 illustrates the overall inverse quantisation process.  After the appropriate inverse quantisation arithmetic the resulting coefficients, F''[v][u], are saturated to yield  F'[v][u] and then a mismatch control operation is performed to give the final reconstructed DCT coefficients, F[v][u].

Note	Attention is drawn to the fact that the method of achieving mismatch control in this specification is different to that employed by ISO/IEC 11172-2.

7.4.1	Intra DC coefficient

The DC coefficients of intra coded blocks shall be inverse quantised in a different manner to all other coefficients.

In intra blocks FÕÕ[0][0] shall be obtained by multiplying QF[0][0] by a constant multiplier, intra_dc_mult, (constant in the sense that it is not modified by either the weighting matrix or the scale factor).  The multiplier is related to the parameter intra_dc_precision that is encoded in the picture coding extension.  TableÊ7-4 specifies the relation between intra_dc_precision and intra_dc_mult.

TableÊ7-4. Relation between intra_dc_precision and intra_dc_mult

| intra_dc_precision | Bits of precision | intra_dc_mult |  | 0 | 8 | 8 |  | 1 | 9 | 4 |  | 2 | 10 | 2 |  | 3 | 11 | 1 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Thus;

7.4.2	Other coefficients

All coefficients other than the DC coefficient of an intra block shall be inverse quantised as specified in this clause.

7.4.2.1	Weighting matrices

When 4:2:0 data is used two weighting matrices are used.  One shall be used for intra macroblocks and the other for non-intra macroblocks.  When 4:2:2 or 4:4:4 data is used, four matrices are used allowing different matrices to be used for luminance and chrominance data.  Each matrix has a default set of values which may be overwritten by down-loading a user defined matrix as explained in 6.2.3.2.

Let the weighting matrices be denoted by W[w][v][u] where w takes the values 0 to 3 indicating which of the matrices is being used. TableÊ7-5 summarises the rules governing the selection of w.

TableÊ7-5. Selection of w

|  | 4:2:0 |  | 4:2:2 and 4:4:4 |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |

luminance

(cc = 0)

chrominance

(cc ­ 0)

luminance

(cc = 0)

chrominance

| (cc ­ 0) |  |
| --- | --- |

intra blocks

| (macroblock_intra = 1) | 0 | 0 | 0 | 2 |  |
| --- | --- | --- | --- | --- | --- |

non-intra blocks

| (macroblock_intra = 0) | 1 | 1 | 1 | 3 |  |
| --- | --- | --- | --- | --- | --- |

7.4.2.2	Quantiser scale factor

The quantisation scale factor is encoded as a fixed length code, quantiser_scale_code.  This indicates the appropriate quantiser_scale to apply in the inverse quantisation arithmetic.

q_scale_type (encoded in the picture coding extension) indicates which of two mappings between quantiser_scale_code and quantiser_scale shall apply.  TableÊ7-6 shows the two mappings between quantiser_scale_code and quantiser_scale.

TableÊ7-6. Relation between quantiser_scale and quantiser_scale_code

|  | quantiser_scale[q_scale_type] |  |  | quantiser_scale_code | q_scale_type = 0 | q_scale_type = 1 |  | 0 | (forbidden) |  |  | 1 | 2 | 1 |  | 2 | 4 | 2 |  | 3 | 6 | 3 |  | 4 | 8 | 4 |  | 5 | 10 | 5 |  | 6 | 12 | 6 |  | 7 | 14 | 7 |  | 8 | 16 | 8 |  | 9 | 18 | 10 |  | 10 | 20 | 12 |  | 11 | 22 | 14 |  | 12 | 24 | 16 |  | 13 | 26 | 18 |  | 14 | 28 | 20 |  | 15 | 30 | 22 |  | 16 | 32 | 24 |  | 17 | 34 | 28 |  | 18 | 36 | 32 |  | 19 | 38 | 36 |  | 20 | 40 | 40 |  | 21 | 42 | 44 |  | 22 | 44 | 48 |  | 23 | 46 | 52 |  | 24 | 48 | 56 |  | 25 | 50 | 64 |  | 26 | 52 | 72 |  | 27 | 54 | 80 |  | 28 | 56 | 88 |  | 29 | 58 | 96 |  | 30 | 60 | 104 |  | 31 | 62 | 112 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

7.4.2.3	Reconstruction formulae

The following equation specifies the arithmetic to reconstruct F''[v][u] from QF[v][u] (for all coefficients except intra DC coefficients).

Note	The above equation uses the Ò/Ó operator as defined in 4.1.

7.4.3	Saturation

The coefficients resulting from the Inverse Quantisation Arithmetic are saturated to lie in the range .  Thus;

7.4.4	Mismatch control

Mismatch control shall be performed by any process equivalent to the following.  Firstly all of the reconstructed, saturated coefficients, F'[v][u] in the block shall be summed.  This value is then tested to determine whether it is odd or even.  If the sum is even then a correction shall be made to just one coefficient; F[7][7]. Thus;

Note 1	It may be useful to note that the above correction for F[7][7] may simply be implemented by toggling the least significant bit of the twos complement representation of the coefficient.  Also since only the ÒoddnessÓ or ÒevennessÓ of the sum is of interest an exclusive OR (of just the least significant bit) may be used to calculate ÒsumÓ.

Note 2	Warning.  Small non-zero inputs to the IDCT may result in zero output for compliant IDCTs.  If this occurs in an encoder, mismatch may occur in some pictures in a decoder that uses a different compliant IDCT. An encoder can avoid this problem by checking the output of its own IDCT.

7.4.5	Summary

In summary the inverse quantisation process is any process numerically equivalent to:

for (v=0; v<8;v++) {

for (u=0; u<8;u++) {

if ( (u==0) && (v==0) && (macroblock_intra) ) {

F''[v][u] = intra_dc_mult * QF[v][u];

} else {

if ( macroblock_intra ) {

F''[v][u] = ( QF[v][u] * W[w][v][u] * quantiser_scale * 2 ) / 32;

} else {

F''[v][u] = ( ( ( QF[v][u] *  2 ) + Sign(QF[v][u]) ) * W[w][v][u]

* quantiser_scale ) / 32;

}

}

}

}

sum = 0;

for (v=0; v<8;v++) {

for (u=0; u<8;u++) {

if ( FÕ'[v][u] > 2047 ) {

FÕ[v][u] = 2047;

} else {

if ( FÕ'[v][u] < -2048 ) {

FÕ[v][u] = -2048;

} else {

FÕ[v][u] = F'Ô[v][u];

}

}

sum = sum + FÕ[v][u];

F[v][u] = FÕ[v][u];

}

}

if ((sum & 1) == 0) {

if ((F[7][7] & 1) != 0) {

F[7][7] = F'[7][7] - 1;

} else {

F[7][7] = F'[7][7] + 1;

}

}

7.5	Inverse DCT

Once the DCT coefficients, F[v][u], are reconstructed, the inverse DCT transform defined in Annex A shall be applied to obtain the inverse transformed values, f[y][x]. These values shall be saturated so that; -256 ² f[y][x] ² 255, for all x, y.

7.5.1	Non-coded blocks and skipped macroblocks

In a macroblock that is not skipped, if pattern_code[i] is one for a given block in the macroblock then coefficient data is included in the bitstream for that block.  This is decoded using as specified in the preceding clauses.

However, if pattern_code[i] is zero, or if the macroblock is skipped, then that block contains no coefficient data.  The sample domain coefficients f[y][x] for such a block shall all take the value zero.

7.6	Motion compensation

The motion compensation process forms predictions from previously decoded pictures which are combined with the coefficient data (from the output of the IDCT) in order to recover the final decoded samples.  Figure 7-4 shows a simplified diagram of this process.

In general up to four separate predictions are formed for each block which are combined together to form the final prediction block p[y][x].

In the case of intra coded macroblocks no prediction is formed so that p[y][x] will be zero.  The saturation shown in Figure 7-4 is still required in order to remove negative values from f[y][x].  Intra coded macroblocks may carry motion vectors known as Òconcealment motion vectorsÓ.  Despite this no prediction is formed in the normal course of events.  This motion vector information is intended for use in the case that bitstream errors preclude the decoding of coefficient information.  The way in which a decoder shall use this information is not specified. The only requirement for these motion vectors is that they shall have the correct syntax for motion vectors.  A description of the way in which these motion vectors may be used can be found in 7.6.3.9.

In the case where a block is not coded, either because the entire macroblock is skipped or the specific block is not coded there is no coefficient data.  In this case f[y][x] is zero and the decoded samples are simply the prediction, p[y][x].

Figure 7-4. Simplified motion compensation process

7.6.1	Prediction modes

There are two major classifications of the prediction mode; field prediction and frame prediction.

In field prediction, predictions are made independently for each field by using data from one or more previously decoded fields.  Frame prediction forms a prediction for the frame from one or more previously decoded frames.  It must be understood that the fields and frames from which predictions are made may themselves have been decoded as either field pictures or frame pictures.

Within a field picture all predictions are field predictions.  However in a frame picture either field predictions or frame predictions may be used (selected on a macroblock-by macroblock basis).

In addition to the major classification of field or frame prediction two special prediction modes are used:

¥	16x8 motion compensation.  In which two motion vectors are used for each macroblock.  The first motion vector is used for the upper 16x8 region, the second for the lower 16x8 region.  In the case of a bidirectionally predicted macroblock a total of four motion vectors will be used since there will be two for the forward prediction and two for the backward prediction.  In this specification 16x8 motion compensation shall only be used with field pictures.

¥	Dual-prime. In which only one motion vector is encoded (in its full format) in the bitstream together with a small differential motion vector. In the case of field pictures two motion vectors are then derived from this information.  These are used to form predictions from two reference fields (one top, one bottom) which are averaged to form the final prediction.  In the case of frame pictures this process is repeated for the two fields so that a total of four field predictions are made. This mode shall only be used in P-pictures where there are no B-pictures between the predicted and reference fields or frames.

7.6.2	Prediction field and frame selection

The selection of which fields and frames shall be used to form predictions shall be made as detailed in this clause.

7.6.2.1	Field prediction

In P-pictures prediction shall be made from the two most recently decoded reference fields.  The simplest case illustrated in Figure 7-5 shall be used when predicting the first picture of a coded frame or when using field prediction within a frame-picture.  In these cases the two reference fields are part of the same reconstructed frame.

Note 1	The reference fields may themselves have been reconstructed by decoding two field-pictures or a single frame-picture.

Note 2	In the case of predicting a field picture, the field being predicted may be either the top field or the bottom field.

Figure 7-5. Prediction of the first field or field prediction in a frame-picture

The case when predicting the second field picture of a coded frame is more complicated because the two most recently decoded reference fields shall be used, and in this case, the most recent reference field was obtained from decoding the first field picture of the coded frame.  Figure 7-6 illustrates the situation when this second picture is the bottom field.   Figure 7-7 illustrates the situation when this second picture is the top field.

Note	The earlier reference field may itself have been reconstructed by decoding a field picture or a frame picture.

Figure 7-6. Prediction of the second field-picture when it is the bottom field

Figure 7-7. Prediction of the second field-picture when it is the top field

Field prediction in B-pictures shall be made from the two fields of the two most recently reconstructed reference frames.  Figure 7-8 illustrates this situation.

Note	The reference frames may themselves have been reconstructed from two field-pictures or a single frame-picture.

Figure 7-8. Field-prediction of B field pictures or B frame pictures

7.6.2.2	Frame prediction

In P-pictures prediction shall be made from the most recently reconstructed reference frame.  This is illustrated in Figure 7-9.

Note	The reference frame may itself have been coded as two field pictures or a single frame picture.

Figure 7-9. Frame-prediction for I-pictures and P-pictures

Similarly frame prediction in B-pictures shall be made from the two most recently reconstructed reference frames as illustrated in Figure 7-10.

Note	The reference frames themselves may each have been coded as either two field pictures or a single frame picture.

Figure 7-10. Frame-prediction for B-pictures

7.6.3	Motion vectors

Motion vectors are coded differentially with respect to previously decoded motion vectors in order to reduce the number of bits required to represent them.  In order to decode the motion vectors the decoder shall maintain four motion vector predictors (each with a horizontal and vertical component) denoted PMV[r][s][t].  For each prediction, a motion vector, vectorÕ[r][s][t] is first derived.  This is then scaled depending on the sampling structure (4:2:0, 4:2:2 or 4:4:4) to give a motion vector, vector[r][s][t], for each colour component.  The meanings associated with the dimensions in this array are defined in TableÊ7-7.

TableÊ7-7. Meaning of indices in PMV[r][s][t], vector[r][s][t] and vectorÕ[r][s][t]

|  | 0 | 1 |  | r | First motion vector in Macroblock | Second motion vector in Macroblock |  | s | Forward motion Vector | Backwards motion Vector |  | t | Horizontal Component | Vertical Component |  | Note: r also takes the values 2 and 3 for derived motion vectors used with dual-prime prediction. Since these motion vectors are derived they do not themselves have motion vector predictors. |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

7.6.3.1	Decoding the motion vectors

Each motion vector component, vectorÕ[r][s][t], shall be calculated by any process that is equivalent to the following one.  Note that the motion vector predictors shall also be updated by this process.

r_size = f_code[s][t] - 1

f = 1 << r_size

high = ( 16 * f ) -  1;

low = ( (-16) * f );

range = ( 32 * f );

if ( (f  == 1) || (motion_code[r][s][t] == 0) )

delta = motion_code[r][s][t] ;

else {

delta = ( ( Abs(motion_code[r][s][t]) - 1 ) * f ) + motion_residual[r][s][t] + 1;

if (motion_code[r][s][t] < 0)

delta = - delta;

}

prediction = PMV[r][s][t];

if ( (mv_format == ÒfieldÓ) && (t==1) && (picture_structure == ÒFrame pictureÓ) )

prediction = PMV[r][s][t] DIV 2;

vectorÕ[r][s][t]= prediction + delta;

if (vectorÕ[r][s][t] < low )

vectorÕ[r][s][t] = vectorÕ[r][s][t] + range;

if (vectorÕ[r][s][t] > high)

vectorÕ[r][s][t] = vectorÕ[r][s][t] - range;

if ( (mv_format == ÒfieldÓ) && (t==1) && (picture_structure == ÒFrame pictureÓ) )

PMV[r][s][t] = vectorÕ[r][s][t] * 2;

else

PMV[r][s][t] = vectorÕ[r][s][t];

The parameters in the bitstream shall be such that the reconstructed differential motion vector, delta, shall lie in the range [low:high]. In addition the reconstructed motion vector, vectorÕ[r][s][t], and the updated value of the motion vector predictor PMV[r][s][t], shall also lie in the range [low : high].

r_size, f, delta, high , low  and range are temporary variables that are not used in the remainder of this specification.

motion_code, motion_residual and mv_format are fields recovered from the bitstream.

r, s and t specify the particular motion vector component being processed as identified in TableÊ7-7.

vectorÕ[r][s][t] is the final reconstructed motion vector for the luminance component of the macroblock.

7.6.3.2	Motion vector restrictions

In frame pictures, the vertical component of field motion vectors shall be restricted so that they only cover half the range that is supported by the f_code that relates to those motion vectors.  This restriction ensures that the motion vector predictors will always have values that are appropriate for decoding subsequent frame motion vectors.  TableÊ7-9 summarises the size of motion vectors that may be coded as a function of f_code.

TableÊ7-9. Allowable motion vector range as a function of f_code[s][t]

f_code[s][t]

Vertical components (t==1) of

field vectors in frame pictures

| All other cases |  | 0 | (forbidden) |  |  | 1 | [-4: +3,5] | [-8: +7,5] |  | 2 | [-8: +7,5] | [-16: +15,5] |  | 3 | [-16: +15,5] | [-32: +31,5] |  | 4 | [-32: +31,5] | [-64: +63,5] |  | 5 | [-64: +63,5] | [-128: +127,5] |  | 6 | [-128: +127,5] | [-256: +255,5] |  | 7 | [-256: +255,5] | [-512: +511,5] |  | 8 | [-512: +511,5] | [-1024: +1023,5] |  | 9 | [-1024: +1023,5] | [-2048: +2047,5] |  | 10-15 | (reserved) |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

7.6.3.3	Updating motion vector predictors

Once all of the motion vectors present in the macroblock have been decoded using the process defined in the previous clause it is sometimes necessary to update other motion vector predictors.  This is because in some prediction modes fewer than the maximum possible number of motion vectors are used.  The remainder of the predictors that might be used in the picture must retain ÒsensibleÓ values in case they are subsequently used.

The motion vector predictors shall be updated as specified in TableÊ7-10 and 7-11.  The rules for updating motion vector predictors in the case of skipped macroblocks are specified in 7.6.6.

Note	It is possible for an implementation to optimise the updating (and resetting) of motion vector predictors depending on the picture type.  For example in a P-picture the predictors for backwards motion vectors are unused and need not be maintained.

TableÊ7-10. Updating of motion vector predictors in frame pictures

| frame_motion_- | macroblock_motion_- |  | macroblock_- |  |  | type | forward | backward | intra | Predictors to Update |  | Frame-basedà | - | - | 1 | PMV[1][0][1:0] = PMV[0][0][1:0]× |  | Frame-based | 1 | 1 | 0 | PMV[1][0][1:0] = PMV[0][0][1:0] |  |  |  |  |  | PMV[1][1][1:0] = PMV[0][1][1:0] |  | Frame-based | 1 | 0 | 0 | PMV[1][0][1:0] = PMV[0][0][1:0] |  | Frame-based | 0 | 1 | 0 | PMV[1][1][1:0] = PMV[0][1][1:0] |  | Frame-basedà | 0 | 0 | 0 | PMV[r][s][t] = 0 ¤ |  | Field-based | 1 | 1 | 0 | (none) |  | Field-based | 1 | 0 | 0 | (none) |  | Field-based | 0 | 1 | 0 | (none) |  | Dual prime | 1 | 0 | 0 | PMV[1][0][1:0] = PMV[0][0][1:0] |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Note:	PMV[r][s][1:0] = PMV[u][v][1:0] means that;

PMV[r][s][1] = PMV[u][v][1] and PMV[r][s][0] = PMV[u][v][0]

×	If concealment_motion_vectors is zero then PMV[r][s][t] is set to zero (for all r, s and t).

à	frame_motion_type is not present in the bitstream but is assumed to be Frame-based

| ¤ (Only occurs in P-picture) PMV[r][s][t] is set to zero (for all r, s and t). See 7.6.3.4 |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |

TableÊ7-11. Updating of motion vector predictors in field pictures

| field_motion_- | macroblock_motion_- |  | macroblock_- |  |  | type | forward | backward | intra | Predictors to Update |  | Field-basedà | - | - | 1 | PMV[1][0][1:0] = PMV[0][0][1:0]× |  | Field-based | 1 | 1 | 0 | PMV[1][0][1:0] = PMV[0][0][1:0] |  |  |  |  |  | PMV[1][1][1:0] = PMV[0][1][1:0] |  | Field-based | 1 | 0 | 0 | PMV[1][0][1:0] = PMV[0][0][1:0] |  | Field-based | 0 | 1 | 0 | PMV[1][1][1:0] = PMV[0][1][1:0] |  | Field-basedà | 0 | 0 | 0 | PMV[r][s][t] = 0 ¤ |  | 16x8 MC | 1 | 1 | 0 | (none) |  | 16x8 MC | 1 | 0 | 0 | (none) |  | 16x8 MC | 0 | 1 | 0 | (none) |  | Dual prime | 1 | 0 | 0 | PMV[1][0][1:0] = PMV[0][0][1:0] |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Note:	PMV[r][s][1:0] = PMV[u][v][1:0] means that;

PMV[r][s][1] = PMV[u][v][1] and PMV[r][s][0] = PMV[u][v][0]

×	If concealment_motion_vectors is zero then PMV[r][s][t] is set to zero (for all r, s and t).

à	field_motion_type is not present in the bitstream but is assumed to be Field-based

| ¤ (Only occurs in P-picture) PMV[r][s][t] is set to zero (for all r, s and t). See 7.6.3.4 |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |

7.6.3.4	Resetting motion vector predictors

All motion vector predictors shall be reset to zero in the following cases:

¥	At the start of each slice.

¥	Whenever an intra macroblock is decoded which has no concealment motion vectors.

¥	In a P-picture when a non-intra macroblock is decoded in which macroblock_motion_forward is zero.

¥	In a P-picture when a macroblock is skipped.

7.6.3.5	Prediction in P-pictures

In P-pictures, in the case that macroblock_motion_forward is zero and macroblock_intra is also zero no motion vectors are encoded for the macroblock yet a prediction must be formed.  If this occurs in a P field picture the following apply;

¥	The prediction mode shall be ÒField-basedÓ

¥	The (field) motion vector shall be zero (0;0)

¥	The motion vector predictors shall be reset to zero

¥	Predictions shall be made from the field of the same parity as the field being predicted.

If this occurs in a P frame picture the following apply;

¥	The prediction mode shall be ÒFrame-basedÓ

¥	The (frame) motion vector shall be zero (0;0)

¥	The motion vector predictors shall be reset to zero

In the case that a P field picture is used as the second field of a frame in which the first field is an I field picture a series of semantic restrictions apply.  These ensure that prediction is only made from the I field picture. These restrictions are;

¥	There shall be no macroblocks that are coded with macroblock_motion_forward zero and macroblock_intra zero.

¥	Dual prime prediction shall not be used.

¥	Field prediction in which motion_vertical_field_select indicates the same parity as the field being predicted shall not be used.

¥	There shall be no skipped macroblocks.

7.6.3.6	Dual prime additional arithmetic

In dual prime prediction one field motion vector (vectorÕ[0][0][1:0]) will have been decoded by the process already described.  This represents the motion vector used to form predictions from the reference field (or reference fields in a frame picture) of the same parity as the prediction being formed.  Here the word ÒparityÓ is used to differentiate the two fields.  The top field has parity zero, the bottom field has parity one.

Figure 7-11. Scaling of motion vectors for dual prime prediction

In order to form a motion vector for the opposite parity (vectorÕ[r][0][1:0]) the existing motion vector is scaled to reflect the different temporal distance between the fields.  A correction is made to the vertical component (to reflect the vertical shift between the lines of top field and bottom field) and then a small differential motion vector is added.  This process is illustrated in Figure 7-11 which shows the situation for a frame picture.

dmvector[0] is the horizontal component of the differential motion vector and dmvector[1] the vertical component.  The two components of the differential motion vector shall be decoded directly using TableÊB-11 and shall take only one of the values -1, 0, +1.

m[parity_ref][parity_pred] is the field distance between the predicted field and the reference field as defined in TableÊ7-12. Òparity_refÓ is the parity of the reference field for which the new motion vector is being computed.  Òparity_predÓ is the parity of the field that shall be predicted.

e[parity_ref][parity_pred] is the adjustment necessary to reflect the vertical shift between the lines of top field and bottom field as defined in TableÊ7-13.

TableÊ7-12. Definition of m[parity_ref][parity_pred]

|  |  | m[parity_ref][parity_pred] |  |  | picture_structure | top_field_first | m[1][0] | m[0][1] |  | 11 (Frame) | 1 | 1 | 3 |  | 11 (Frame) | 0 | 3 | 1 |  | 01 (Top Field) | - | 1 | - |  | 10 (Bottom Field) | - | - | 1 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

TableÊ7-13. Definition of e[parity_ref][parity_pred]

| parity_ref | parity_pred | e[parity_ref][parity_pred] |  | 0 | 0 | 0 |  | 0 | 1 | +1 |  | 1 | 0 | -1 |  | 1 | 1 | 0 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

The motion vector (or motion vectors) used for predictions of opposite parity shall be computed as follows;

vectorÕ[r][0][0] = ((vectorÕ[0][0][0] * m[parity_ref][parity_pred])//2) + dmvector[0];

vectorÕ[r][0][1] = ((vectorÕ[0][0][1] * m[parity_ref][parity_pred])//2)

+ e[parity_ref][parity_pred] + dmvector[1];

In the case of field pictures only one such motion vector is required and here r=2.  Thus the (encoded) motion vector used for the same parity prediction is vectorÕ[0][0][1:0] and the motion vector used for the opposite parity prediction is vectorÕ[2][0][1:0].

In the case of frame pictures two such motion vectors are required.  Both fields use the encoded motion vector (vectorÕ[0][0][1:0]) for predictions of the same parity.  The top field shall use vectorÕ[2][0][1:0] for opposite parity prediction and the bottom field shall use vectorÕ[3][0][1:0] for opposite parity prediction.

7.6.3.7	Motion vectors for chrominance components

The motion vectors calculated in the previous clauses refer to the luminance component where;

vector[r][s][t] = vectorÕ[r][s][t]		(for all r, s and t)

For each of the two chrominance components the motion vectors shall be scaled as follows:

4:2:0	Both the horizontal and vertical components of the motion vector are scaled by dividing by two:

vector[r][s][0] = vectorÕ[r][s][0] / 2;

vector[r][s][1] = vectorÕ[r][s][1] / 2;

4:2:2	The horizontal component of the motion vector is scaled by dividing by two, the vertical component is not altered:

vector[r][s][0] = vectorÕ[r][s][0] / 2;

vector[r][s][1] = vectorÕ[r][s][1];

4:4:4	The motion vector is unmodified:

vector[r][s][0] = vectorÕ[r][s][0];

vector[r][s][1] = vectorÕ[r][s][1];

7.6.3.8	Semantic restrictions concerning predictions

It is a requirement on the bitstream that it shall only demand of a decoder that predictions shall be made from slices actually encoded in a reference frame or reference field.  This rule applies even for skipped macroblocks and macroblocks in P-pictures in which a zero motion vector is assumed (as explained in 7.6.3.5).

Note	As explained in 6.1.3 it is, in general, not necessary for the slices to cover the entire picture.  However in many defined levels of defined profiles the Òrestricted slice structureÓ is used in which case the slices do cover the entire picture.  In this case the semantic rule may be more simply stated; Òit is a restriction on the bitstream that reconstructed motion vectors shall not refer to samples outside the boundary of the coded picture.Ó

7.6.3.9	Concealment motion vectors

Concealment motion vectors are motion vectors that may be carried by intra macroblocks for the purpose of concealing errors should data errors preclude decoding the coefficient data.  A concealment motion vector shall be present for all intra macroblocks if (and only if) concealment_motion_vectors (in the picture_coding_extension() ) has the value one.

In the normal course of events no prediction shall be formed for such macroblocks (as would be expected since macroblock_intra = 1).  This specification does not specify how error recovery shall be performed.  However it is a recommendation that concealment motion vectors are suitable for use by a decoder that performs concealment by forming predictions as if the following flags that control the formation of predictions have the indicated values;

¥	In a field picture;	field_motion_type = ÒField-based predictionÓ

¥	In a frame picture;	frame_motion_type = ÒFrame-based predictionÓ

Note	If concealment is used in an I-picture then the decoder should perform prediction in a similar way to a P-picture.

Concealment motion vectors are intended for use in the case that a data error results in information being lost.  There is therefore little point in encoding the concealment motion vector in the macroblock for which it is intended to be used since if the data error results in the need for error recovery it is very likely that the concealment motion vector itself would be lost or corrupted  As a result the following semantic rules are appropriate.

¥	For all macroblocks except those in the bottom row of macroblocks concealment motion vectors should be appropriate for use in the macroblock that lies vertically below the macroblock in which the motion vector occurs.

¥	When the motion vector is used with respect to the macroblock identified in the previous rule a decoder must assume that the motion vector may refer to samples outside of the slices encoded in the reference frame or reference field.

For all macroblocks in the bottom row of macroblocks the reconstructed concealment motion vectors will not be used. Therefore the motion vector (0;0) may be used to reduce unnecessary overhead.

7.6.4	Forming predictions

Predictions are formed by reading prediction samples from the reference fields or frames. A given sample is predicted by reading the corresponding sample in the reference field or frame offset by the motion vector.

A positive value of the horizontal component of a motion vector indicates that the prediction is made from samples (in the reference field/frame) that lie to the right of the samples being predicted.

A positive value of the vertical component of a motion vector indicates that the prediction is made from samples (in the reference field/frame) that lie the below the samples being predicted.

All motion vectors are specified to an accuracy of one half sample.  Thus if a component of the motion vector is odd, the samples will be read from mid-way between the actual samples in the reference field/frame.  These half-samples are calculated by simple linear interpolation from the actual samples.

In the case of field-based predictions it is necessary to determine which of the two available fields to use to form the prediction.  In the case of dual-prime this is specified in that a motion vector is derived for both of the fields and a prediction is formed from each.  In the case of field-based prediction and 16x8ÊMC an additional bit, motion_vertical_field_select, is encoded to indicate which field to use.

If motion_vertical_field_select is zero then the prediction is taken from the top reference field.

If motion_vertical_field_select is one then the prediction is taken from the bottom reference field.

For each prediction block the integer sample motion vectors int_vec[t] and the half sample flags half_flag[t] shall be formed as follows;

for (t=0; t<2; t++) {

int_vec[t] = vector[r][s][t] DIV 2;

if ((vector[r][s][t] - (2 * int_vec[t]) != 0)

half_flag[t] = 1;

else

half_flag[t] = 0;

}

Then for each sample in the prediction block the samples are read and the half sample prediction applied as follows;

if ( (! half_flag[0] )&& (! half_flag[1]) )

pel_pred[y][x] = pel_ref[y + int_vec[1]][x + int_vec[0]] ;

if ( (! half_flag[0] )&& half_flag[1] )

pel_pred[y][x] = ( pel_ref[y + int_vec[1]][x + int_vec[0]] +

pel_ref[y + int_vec[1]+1][x + int_vec[0]] ) // 2;

if ( half_flag[0]&& (! half_flag[1]) )

pel_pred[y][x] = ( pel_ref[y + int_vec[1]][x + int_vec[0]] +

pel_ref[y + int_vec[1]][x + int_vec[0]+1] ) // 2;

if ( half_flag[0]&& half_flag[1] )

pel_pred[y][x] = ( pel_ref[y + int_vec[1]][x + int_vec[0]] +

pel_ref[y + int_vec[1]][x + int_vec[0]+1] +

pel_ref[y + int_vec[1]+1][x + int_vec[0]] +

pel_ref[y + int_vec[1]+1][x + int_vec[0]+1] ) // 4;

where pel_pred[y][x] is the prediction sample being formed and pel_ref[y][x] are samples in the reference field or frame.

7.6.5	Motion vector selection

TableÊ7-14 shows the prediction modes used in field pictures and TableÊ7-15 shows the predictions used in frame pictures.  In each table the motion vectors that are present in the bitstream are listed in the order in which they appear in the bitstream.

TableÊ7-14. Predictions and motion vectors in field pictures

| field_ |  |  | macro- |  |  |  | motion_ | macroblock_motion_- |  | block_- |  |  |  | type | forward | backward | intra | Motion vector | Prediction formed for |  | Field-basedà | - | - | 1 | vector'[0][0][1:0]× | None (motion vector is for concealment) |  | Field-based | 1 | 1 | 0 | vector'[0][0][1:0] | whole field, forward |  |  |  |  |  | vector'[0][1][1:0] | whole field, backward |  | Field-based | 1 | 0 | 0 | vector'[0][0][1:0] | whole field, forward |  | Field-based | 0 | 1 | 0 | vector'[0][1][1:0] | whole field, backward |  | Field-basedà | 0 | 0 | 0 | vector'[0][0][1:0]*¤ | whole field, forward |  | 16x8 MC | 1 | 1 | 0 | vector'[0][0][1:0] | upper 16x8 field, forward |  |  |  |  |  | vector'[1][0][1:0] | lower 16x8 field, forward |  |  |  |  |  | vector'[0][1][1:0] | upper 16x8 field, backward |  |  |  |  |  | vector'[1][1][1:0] | lower 16x8 field, backward |  | 16x8 MC | 1 | 0 | 0 | vector'[0][0][1:0] | upper 16x8 field, forward |  |  |  |  |  | vector'[1][0][1:0] | lower 16x8 field, forward |  | 16x8 MC | 0 | 1 | 0 | vector'[0][1][1:0] | upper 16x8 field, backward |  |  |  |  |  | vector'[1][1][1:0] | lower 16x8 field, backward |  | Dual prime | 1 | 0 | 0 | vector'[0][0][1:0] | whole field, from same parity, forward |  |  |  |  |  | vector'[2][0][1:0]* | whole field, from opposite parity, forward |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Note:	Motion vectors are listed in the order they appear in the bitstream

×	the motion vector is only present if concealment_motion_vectors is one

à	field_motion_type is not present in the bitstream but is assumed to be Field-based

*	These motion vectors are not present in the bitstream

These motion vectors are derived from vectorÕ[0][0][1:0] as described in 7.6.3.6

| ¤ The motion vector is taken to be (zero, zero) as explained in 7.6.3.5. |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |

TableÊ7-15. Predictions and motion vectors in frame pictures

| frame_- |  |  | macro- |  |  |  | motion_- | macroblock_motion_- |  | block_- |  |  |  | type | forward | backward | intra | Motion vector | Prediction formed for |  | Frame-basedà | - | - | 1 | vector'[0][0][1:0]× | None (motion vector is for concealment) |  | Frame-based | 1 | 1 | 0 | vector'[0][0][1:0] | frame, forward |  |  |  |  |  | vector'[0][1][1:0] | frame, backward |  | Frame-based | 1 | 0 | 0 | vector'[0][0][1:0] | frame, forward |  | Frame-based | 0 | 1 | 0 | vector'[0][1][1:0] | frame, backward |  | Frame-basedà | 0 | 0 | 0 | vector'[0][0][1:0]*¤ | frame, forward |  | Field-based | 1 | 1 | 0 | vector'[0][0][1:0] | top field, forward |  |  |  |  |  | vector'[1][0][1:0] | bottom field, forward |  |  |  |  |  | vector'[0][1][1:0] | top field, backward |  |  |  |  |  | vector'[1][1][1:0] | bottom field, backward |  | Field-based | 1 | 0 | 0 | vector'[0][0][1:0] | top field, forward |  |  |  |  |  | vector'[1][0][1:0] | bottom field, forward |  | Field-based | 0 | 1 | 0 | vector'[0][1][1:0] | top field, backward |  |  |  |  |  | vector'[1][1][1:0] | bottom field, backward |  | Dual prime | 1 | 0 | 0 | vector'[0][0][1:0] | top field, from same parity, forward |  |  |  |  |  | vector'[0][0][1:0] | bottom field, from same parity, forward |  |  |  |  |  | vector'[2][0][1:0]* | top field, from opposite parity, forward |  |  |  |  |  | vector'[3][0][1:0]* | bottom field, from opposite parity, forward |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Note:	Motion vectors are listed in the order they appear in the bitstream

×	the motion vector is only present if concealment_motion_vectors is one

à	frame_motion_type is not present in the bitstream but is assumed to be Frame-based

*	These motion vectors are not present in the bitstream

These motion vectors are derived from vectorÕ[0][0][1:0] as described in 7.6.3.6

| ¤ The motion vector is taken to be (zero, zero) as explained in 7.6.3.5 |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |

7.6.6	Skipped Macroblocks

In skipped macroblocks (where macroblock_address_increment is greater than 1) the decoder has neither DCT coefficient information nor motion vector information.  The decoder shall form a prediction for such macroblocks which shall then be used as the final decoded sample values.

The handling of skipped macroblocks is different between P-pictures and B-pictures.  In addition the process differs between field pictures and frame pictures.

There shall be no skipped macroblocks in I-pictures except when;

either	picture_spatial_scalable_extension() follows the picture_header() of the current picture.

or	sequence_scalable_extension() is present in the bitstream and scalable_mode = ÒSNR scalabilityÓ.

7.6.6.1	P field picture

¥	The prediction shall be made as if field_motion_type is ÒField-basedÓ

¥	The prediction shall be made from the field of the same parity as the field being predicted.

¥	Motion vector predictors shall be reset to zero.

¥	The motion vector shall be zero.

7.6.6.2	P frame picture

¥	The prediction shall be made as if frame_motion_type is ÒFrame-basedÓ

¥	Motion vector predictors shall be reset to zero.

¥	The motion vector shall be zero.

7.6.6.3	B field picture

¥	The prediction shall be made as if field_motion_type is ÒField-basedÓ

¥	The prediction shall be made from the field of the same parity as the field being predicted.

¥	The direction of the prediction forward/backward/bi-directional shall be the same as the previous macroblock.

¥	Motion vector predictors are unaffected.

¥	The motion vectors are taken from the appropriate motion vector predictors.  Scaling of the motion vectors for colour components shall be performed as described in 7.6.3.7.

7.6.6.4	B frame picture

¥	The prediction shall be made as if frame_motion_type is ÒFrame-basedÓ

¥	The direction of the prediction forward/backward/bi-directional shall be the same as the previous macroblock.

¥	Motion vector predictors are unaffected.

¥	The motion vectors are taken directly from the appropriate motion vector predictors.  Scaling of the motion vectors for colour components shall be performed as described in 7.6.3.7.

7.6.7	Combining predictions

The final stage is to combine the various predictions together in order to form the final prediction blocks.

It is also necessary to organise the data into blocks that are either field organised or frame organised in order to be added directly to the decoded coefficients.

The transform data is either field organised or frame organised as specified by dct_type.

7.6.7.1	Simple frame predictions

In the case of simple frame predictions the only further processing that may be required is to average forward and backward predictions in B-pictures.  If pel_pred_forward[y][x] is the forwards prediction sample and pel_pred_backward[y][x] is the corresponding backward prediction then the final prediction sample shall be formed as;

pel_pred[y][x] = (pel_pred_forward[y][x] + pel_pred_backward[y][x])//2;

The predictions for chrominance components of 4:2:0, 4:2:2 and 4:4:4 formats shall be of size 8 samples by 8 lines, 8 samples by 16 lines and 16 samples by 16 lines respectively.

7.6.7.2	Simple field predictions

In the case of simple field predictions (i.e. neither 16x8 or dual prime) the only further processing that may be required is to average forward and backward predictions in B-pictures.  This shall be performed as specified for ÒFrame predictionsÓ in the previous clause.

The predictions for chrominance components of 4:2:0, 4:2:2 and 4:4:4 formats for each field shall be of size 8 samples by 4 lines, 8 samples by 8 lines and 16 samples by 8 lines respectively.

7.6.7.3	16x8 Motion compensation

In this prediction mode separate predictions are formed for the upper 16x8 region of the macroblock and the lower 16x8 region of the macroblock.

The predictions for chrominance components, for each 16x8 region, of 4:2:0, 4:2:2 and 4:4:4 formats shall be of size 8 samples by 4 lines, 8 samples by 8 lines and 16 samples by 8 lines respectively.

7.6.7.4	Dual prime

In dual prime mode two predictions are formed for each field in an analogous manner to the backward and forward predictions in B-pictures.  If pel_pred_same_parity[y][x] is the prediction sample from the same parity field and pel_pred_opposite_parity[y][x] is the corresponding sample from the opposite prediction then the final prediction sample shall be formed as;

pel_pred[y][x] = (pel_pred_same_parity[y][x] + pel_pred_opposite_parity[y][x])//2;

In the case of dual prime prediction in a frame picture, the predictions for chrominance components of each field of 4:2:0, 4:2:2 and 4:4:4 formats shall be of size 8 samples by 4 lines, 8 samples by 8 lines and 16 samples by 8 lines respectively.

In the case of dual prime prediction in a field picture, the predictions for chrominance components of 4:2:0, 4:2:2 and 4:4:4 formats shall be of size 8 samples by 8 lines, 8 samples by 16 lines and 16 samples by 16 lines respectively.

7.6.8	Adding prediction and coefficient data

The prediction blocks have been formed and reorganised into blocks of prediction samples p[y][x] which match the field/frame structure used by the transform data blocks.

The transform data f[y][x] shall be added to the prediction data and saturated to form the final decoded samples d[y][x] as follows;

for (y=0; y<8; y++) {

for (x=0; x<8; x++) {

d[y][x] = f[y][x]+p[y][x];

if (d[y][x] < 0) d[y][x] = 0;

if (d[y][x] > 255) d[y][x] = 255;

}

}

7.7	S

# Footnotes

patial scalability

This clause specifies the additional decoding p